## Slide 1: This is Systems Engineering
Secondary Information Goes Here
This Session
Defines Systems Engineering and its benefits
Explains the relationship between Systems Thinking, Approach and Engineering
Introduces Systems Thinking as the foundation of Systems Engineering
Provides an overview of Systems Thinking
Introduces the basic Systems Engineering process, tools and role of people

## Slide 2: In Simple Terms – Systems Engineering is about:
I WANT
WOW!
turning into
Customer/User Requirements
The Solution
It’s about design

## Slide 3: Traditional Design
problem
solution
When given a problem it is human nature to immediately think of solutions. We want an outline answer we can work on. This concept design solution often based on prior experience where previous solutions are adapted to fit the current problem or assumptions are made unconsciously about a solution.

## Slide 4: Approaches – The Choices
Photocopying

## Slide 5: Photocopying
Take an existing design (that works!) and enlarge or reduce to fit the requirements
Benefits
  Have a solution quickly
  Previous one worked so risk are considered low
Issues
  Scales laws are often to high powers (X3 or X4) – we assume linearity but it isn’t and undesirable behaviour occurs
  Requirements not fully understood and the “photocopied” design doesn't work – redesign and greater costs

## Slide 6
Trent 700
Fan Dia 97.4’’
Thrust 70,000lb
Trent 900
Fan Dia 116’’
Thrust 85,000lb
x1.19

## Slide 7: Approaches – The Choices
Photocopying
Flower
Arranging

## Slide 8: Flower Arranging
Take some nice looking components and arrange that to build a bigger thing
Benefits
  Uses know and trusted components
  Good fun
Issues
  Unexpected behaviour
  Relies on luck (can be mitigated by analysis i.e. design analyse redesign analyse, re-redesign analyse) – therefore costly

## Slide 10: Approaches – The Choices
Photocopying
Flower
Arranging
Evolutionary

## Slide 11: Evolution
Successive modifications to an existing design quite often involving replacing one or more sub-systems
Benefits
  Perceived as tried and tested – trustworthy
  Continuous improvement
Issues
  Improvements are incremental – limited opportunity for step change
  Shortfalls in performance due to unexpected interactions

## Slide 12: Evolutionary
In September 2013, Microsoft announced that it would acquire Nokia's mobile phone business
Size
Sales
2007

## Slide 13: Approaches – The Choices
Photocopying
Flower
Arranging
Evolutionary
Pet Pony

## Slide 14: Pet Pony
A idea, usually a piece of technology, that an individual wants to use come what may
Benefits
  Might be the next “wheel”
Issues
  More logical, risk adverse approaches overridden
  Extensive late re-design or having to live with a sub-standard system
Sir Clive Sinclair was so convinced that the C5 was the future of personal transport he spent £12M of his own money (1985) – equivalent to £100m today

## Slide 15: There’s many more
Notes: Apple Newton – this first ipad! Ridiculed in the press for its expense and lack of flexibility compared to a note pad and pencil
Digital Audio Tape: never really took off like compact cassettes – even though technically it was rather good.

## Slide 16: Analysis to the Rescue
Engineering Analysis
problem
solution
When given a problem it is human nature to immediately think of solutions. We want an outline answer we can work on. This concept design solution often based on prior experience where previous solutions are adapted to fit the current problem or assumptions are made unconsciously about a solution. It is also human nature to stop once we have found the first adequate solution and begin:

## Slide 17: Analysis and Engineering Design
Analysis is the core of traditional engineering design where we use engineering science to understand
Take apart the design
Understand the parts
Combine the understand of the parts to understand the whole
Having jumped to a solution

## Slide 18: The Facts
We Experience
  Redesign
  Late
  Cost overruns
  Testing
  Firefighting
  Heroes
We Believe
  Fast
  The only way
  Worked in the past
  Get there in the end

## Slide 19: Conclusion
We no longer have the time or the money to rely on traditional “solutioneering” approaches (1 in 10 chance of getting it right1)
We need:
  to identify and fix issues early
  a through-life view – design for the life cycle
  a concurrent (Product, Manufacturing, Operation, Support, Disposal) view
  a customer focused view to deliver performance, quality and cost
We need a Systems Approach to Systems Design
1Elm J.P and Goldenson D.R “The Business Case for Systems Engineering Study: Results of the Systems Engineering Effectiveness Survey” November 2012 SPECIAL REPORT, CMU/SEI-2012-SR-009, Carnegie Mellon University

## Slide 20: A Systems Approach to Systems Design
Rigorous process based on Systems Thinking
Benefits
  97% success rate (Carnegie Mellon University, 2012)
Issues
  Perceived to be slow – but actually faster because of low rate of avoidable re-design

## Slide 21: Consequence of Solutioneering?
Form two lines standing opposite each other
Each team member should use one finger to support the paper tube from the underside
Keeping every finger in constant contact with underside of the tube, as a team, lower it to the ground
Time 10 minutes
Notes: This exercise is described in the exercise trainer notes.

## Slide 22
.. and is why
Systems Engineering
is absolutely essential
The “helium” tube exercise illustrates what is called
Emergent
Behaviour
Note: 1. Changing a person would have little effect on the behaviour of the team
2. Rhetoric will have little effect
3. Organization of the team has the biggest effect

## Slide 23: Emergence and Emergent Behaviour
The properties of the pen as a whole are not found in any of the individual components. Only when the components are assembled in the right sequence and the right place do we get the desirable emergent behaviour of being able to make marks on paper
All systems display emergent behaviour – this can be DESIRABLE and/or UNDESIRABLE!

## Slide 24: A Few Problems

## Slide 26: A Few Problems
In all these examples the issues were:
Discovered late on: - they emerged
Expensive: - because they were discovered late
Avoidable:

## Slide 27: Problems Happen Everywhere

## Slide 28: Desirable and Undesirable Emergence
We DESIRE emergent behaviour in our products and services but we can also get UNDESIRABLE emergent behaviour
Undesirable emergent behaviour has three causes
  Variation: unexpected cliff edge performance where small variations cause a significant change in behaviour
  Sub-optimisation: unexpected low performance – the mistaken belief that the “best” system must have the “best components”
  Dynamic: unexpected time related behaviour - we assume things will carry on in the same way – they don’t
Emergent behaviour is a consequence of bringing together the components of a system. Therefore to understand and predict emergent behaviour we need to consider the WHOLE and how the components INTERACT with each other. This is obvious …….
BUT …..

## Slide 29: We put our effort in the Wrong place
Cost to
Fix (£/$)
Requirements
Engineering
Design
Development
Production
Customer
use
This is where
we tend to look
This is where
we should
put our effort
Easy to see
because
Difficult and
costly to fix
BUT
Easy and
cheaper to fix
because
Difficult to see
and predict
BUT
Errors found late on
are caused very early on
Much of the effort in Systems Engineering is expended early on.
Pre-work NOT
Re-work
Source GE DFSS course

## Slide 30: Why is it Difficult to See Issues Early?
When undesirable emergent behaviour appears, hindsight shows the actual cause to be “obvious”
So why did we not spot it earlier?
There are several interrelated reasons
  Complexity
  Functional Divides
  Mind set
  Project Management/Life Cycle Management
We are going to explore a couple of the reasons

## Slide 31: Exercise: Complexity and Humans
You are about to be shown a series of 4 slides
Each slide presents a sentence
Your task is to count the number of occurrences of the letter “f” in each sentence
Each sentence will become longer – but you will be given pro-rata more time in which to count
Time 5 minutes
How many f’s
Slide
A
B
D
C
Count
Notes: This exercise is described in the exercise trainer notes.

## Slide 32
Systems Engineering is the foundation of future success.
A

## Slide 33
Followers of Systems Engineering offer a lot of hope for the future prosperity of the country.
B

## Slide 34
Those organizations that follow Systems Engineering rigorously reap significant benefits in terms of profitability, performance and on time delivery of
of products that both satisfy and delight their customers.
C

## Slide 35
The application of Systems Engineering approaches in the design of systems, that permit sustained, reliable, full spectrum operation, in a wide range of future operating environments, has been demonstrated time after time to deliver substantial business advantage in highly competitive narrow markets by offering non-ephemeral holistic solutions of a unique countenance that totally satisfy multi-stakeholder customers.
D

## Slide 36
Systems Engineering is the foundation of future success.
A

## Slide 37
Followers of Systems Engineering offer a lot of hope for the future prosperity of the country.
B

## Slide 38
Those organizations that follow Systems Engineering rigorously, reap significant benefits in terms
of profitability, performance and
on time delivery of
of products that both satisfy and delight their customers.
C

## Slide 39
The application of Systems Engineering approaches in the design of systems, that permit sustained, reliable, full spectrum operation, in a wide range of future operating environments, has been demonstrated time after time to deliver substantial business advantage in highly competitive narrow markets by offering non-ephemeral holistic solutions of a unique countenance that totally satisfy multi-stakeholder customers.
D

## Slide 40: The Other Mistake
Those organizations that follow Systems Engineering rigorously, reap significant benefits in terms of profitability, performance and on time delivery of
of products that both satisfy and delight their customers.
C

## Slide 41: Complexity
Complexity lies at the heart of the problem because humans cannot handle complexity
In order to satisfy customer needs and expectations, organizations are designing increasingly more complex products and services
This increased complexity has resulted in problems and even failures that demonstrate symptoms of:
  Late delivery
  Cost overruns
  Performance shortfalls
The increased complexity increases the opportunity for an error and makes errors more difficult to find. These errors, if undetected, will result in undesirable emergent behaviour
Pick any product, including service based products, and as it evolved its complexity will have increased

## Slide 42: Our Brain
Pre-frontal Cortex
Limbic System
Brain Stem
Miller showed that this has a processing limitation of 7 +/- 2
But we can “chunk” – grouping information together into chunks of 7+/- 2
Notes: George Miller who in his 1956 seminal paper "The Magical Number Seven, Plus or Minus Two: Some Limits on Our Capacity for Processing Information" did what said on the tin. In simple terms all humans have a processing limit and when faced with complexity beyond this limit we make mistakes, we start to miss things.
However, this processing limitation can be overcome by “chunking”. This is where we group thinks together to form “chunks” and as long as we stick to the 7 +/- 2 we can comprehend any level of complexity.

## Slide 43: Emergence is the Future
Products and services WILL get more complex and therefore issues of undesirable emergent behaviour are going to INCREASE
Organizations no longer provide just a product or service but a cradle to grave solution comprising several interrelated and interdependent systems each of which is becoming increasingly more complex compounding the issues of emergent behaviour
Unless we do something

## Slide 46: Mind Set
Source GEC
DID ANYBODY YOU
’
RE
RESPONSIBLE FOR
MESS WITH IT?
DID ANYBODY YOU
’
RE
RESPONSIBLE FOR
MESS WITH IT?
DID YOU MESS
WITH IT?
WITH IT?
START
DOES THE DAMN
THING WORK?
DOES THE DAMN
THING WORK?
DON
’
T MESS
WITH IT
YOU IDIOT
DOES ANYBODY
KNOW YOU MESSED
WITH IT?
THE END
QUIT
CAN IT BE FIXED
BEFORE YOUR BOSS
FINDS OUT?
IT
’
S YOUR
LUCKY DAY
YOU REALLY
ARE AN IDIOT
WILL YOU CATCH
HELL ANYWAY?
NAIL THEM
NAIL THEM
YOU
’
RE IN IT UP
TO YOUR NECK
WILL YOU
QUIT?
DUMP IT
IN THE SKIP
YOU
’
RE
FIRED
YES
NO
YES
YES
YES
YES
NO
NO
NO
NO
NO
NO
YES
HIDE IT
YES

## Slide 47: Mind Set
Mind Set plays an important role at two levels:
  Individual level - e.g. “FLY” locked-in thinking
  Organizational – e.g. “hide it”
As products, processes and services get more complex and functional divides persist, mind set is an increasingly important factor in not uncovering undesirable emergent behaviour
Unless we do something
Quote from NASA
“The biggest advantage of not doing Systems Engineering is that failure takes us by surprise”

## Slide 48: Complexity, Mind Set and Emergence
Human kind has only developed two approaches to handling complexity:
    Reductionism
    Systems Thinking

## Slide 49: Managing Complexity: Reductionism
Rene Descartes
  “I think Therefore I am”
Discourse on Method and the Meditations …..
  “to divide each of the difficulties under examination into as many parts as possible, and as might be necessary for its adequate solution.”
P
P
P
P
P
P
P
P
P

## Slide 50: Handling Emergence
The only known way to handle issues of emergence, caused by complexity (and the other reasons) is to view the situation (the product, process, or service) as a system and apply Systems Thinking in an organized and disciplined way … and do it early
The beauty of Systems thinking is that it provides a very powerful framework for understanding complex situations by:
  simplifying and clarifying situations to understand the key aspects
  allowing different aspects and perceptions to be portrayed and considered simultaneously to understand and predict emergent behaviour
  looking for dependencies and influences between elements to understand and predict emergent behaviour
  bringing experience to bear upon a situation to understand and predict emergent behaviour

## Slide 51: What is Systems Thinking
Applying the concept of a system to a situation in order to gain insight and understanding

## Slide 52: Who does Systems Thinking
Systems Thinking has and can be applied to every discipline
Some of mankind’s greatest achievements have come about from systems thinking:
  Isaac Newton
  John Maynard Keynes
  Albert Einstein
  Charles Darwin
  Barnes Wallis
  W Edwards Deming
Anybody
Most humans are not natural Systems Thinkers, we have to work hard to do Systems Thinking

## Slide 53: Systems Thinking, Systems Approach and Systems Engineering
Systems Thinking is:
Applying the concept of a system to a situation in order to gain insight and understanding
Systems Approach is:
Applying Systems Thinking in a systematic and repeatable manner
Systems Engineering is:
Applying a Systems Approach to the creation of a system

## Slide 54: The Beauty and Power of Systems Thinking
In Systems Thinking we treat the situation as a system
Product, Process, Service
We can do this even if the situation is NOT a system! This makes it truly universal
We assume that the situation has all the properties and characteristics of a system and explore these to gain more understanding and make predictions about behaviour both desirable and undesirable
Let’s have a look at some of these properties and characteristics of a system

## Slide 55: The Basis of Systems Thinking: The System
An assembly of components, connected together in an organized way to achieve something that is a consequence of the whole
Peter Checkland – Lancaster University
This definition of a system allows for the development of a number of characteristics and properties.
Note: this is not the only definition of a system there are many others but, generally, they all agree that a system comprises three key ingredients:
  Components
  Interconnections
  Purpose
Notes: This is not the only definition of a system; there are many more. A few for example include:
“A System is a set of entities, real or abstract, comprising a whole where each component interacts with or is related to at least one other component and they all serve a common objective” Source: Wikipedia
“An interacting combination of elements to accomplish a defined objective. These include hardware, software, firmware, people, information, techniques, facilities, services, and other support elements.” Source INCOSE Systems Engineering Handbook
“An integrated composite of people, products, and processes that provide a capability to satisfy a stated need or objective” Source: Mil-Std 499B)
“A set of interrelated components which interact with one another in an organized fashion toward a common purpose” Source: NASA Systems Engineering Handbook)
The fact there is no universally agreed definition of a system is irritating but on a practical level it makes little difference since it is what these definition imply that is important . The definition used in this book is that defined by Peter Checkland.
References:
Checkland P. “Systems Thinking, Systems Practice, 1999, Wiley, ISBN 0-471-98606-2
The updated version of Peter Checkland’s ground breaking text on Soft System Methodologies. Rather academic so it’s hard to find the useful bits
Checkland P. Scholes J. Soft Systems Methodology in Action, 1990, John Wiley, ISBN0-471-98605-4
Much more readable than Checkland’s book

## Slide 56: Systems Thinking: Some Key Concepts
Anything can be treated as a system
  A system is an assembly of components, connected together in an organized way to form a whole, this showing properties of the whole, rather than properties of the components
Systems are made up of Subsystems
  Whenever we look “inside” the chosen system of interest we see further smaller systems or subsystems
  Whenever we look outside the chosen system of interest we see that it is part of a larger system
All systems seek to achieve a PURPOSE
  Every system has a purpose that defines fundamentally what it has to do
  Humans tend not to think about purpose explicitly – but implicitly through the thing that achieves the purpose
All systems have CONTEXT
  Every system has context that defines the environment and constraints that impact upon that system
  System context often restricts the solution options that satisfy the purpose

## Slide 57: One More Key Systems Concept
Reinforcing (positive) Feedback: successive changes add to previous changes in the same direction
Balancing (negative) Feedback: resist change in one direction by producing change in the opposite direction
Everything is connected to everything else
The whole is greater (or less than) the sum of parts not because of the parts, but because of the connections between the parts. Systems Thinkers care more about what happens between the components of the system than the components themselves

## Slide 58: System Purpose
All systems seek to achieve a purpose
The purpose is a property of the whole and not found in any of the components
Some systems have more than one purpose
The purpose demands the achievement of lower level purposes as a consequence of the immutable laws of the universe (physics, chemistry etc.)
These lower level purposes in turn demand even lower level purposes which .... BUT it is rarely a simple hierarchy
People who use, or are part of, a system are often totally unaware of its purpose. Moreover, when asked, different users have different, and even sometimes conflicting, views as to the exact nature of the purpose
Rather than talk in sub-purposes we invent taxonomies

## Slide 59
What is the purpose of a pen?

## Slide 60: Exercise: Purpose
In small teams
  Work together to determine the purpose of the listed items
  Be prepared to share your answer with the whole class
Time 15 minutes

## Slide 61: Purposeful Thinking
Defining the purpose of a system is not easy!
The purpose of a system is often a sentence or two – it’s easier to refer to the object!
WE ARE OBJECT ORIENTED we have been brought up from a early age to talk about things and NOT what they DO
IN SYSTEMS THINKING (and ENGINEERING) WE THINK ABOUT THE
PURPOSE

## Slide 62
A key question when Systems Thinking is
What is the purpose?

## Slide 63: System Context
All systems have context which depends on:
  The purpose
  The application (the bigger task or job which the system is part of)
  The environment of the system
  The observer
    an understanding of a system depends upon the perception of the observer. A tax payer will have a different perception of the “Tax System” to the tax collector or government official who is going to spend the tax revenue.

## Slide 64: Does Context Matter
The PURPOSE is the same in each situation “turn thoughts into marks on paper”
BUT can the same pen solution be used in all three situations?
Context matters and we need to be able to understand it by defining the extent of the system of interest and its environment

## Slide 65: Context is more than just the environment
Recording event in a journal
Flip Chart in a Training class
Record of birth in a Registry Office
The purpose is the same, but the bigger need or application is different

## Slide 66: Properties and Characteristics of Systems System Boundary and Environment
A system has a boundary that defines the extent of the system.
Environment
Universe
System
Boundary
System
Inputs
Outputs
The environment of a system is that part of the outside world which significantly interacts with it and impacts upon it. Usually by being the source of system inputs and destination of system outputs. A system’s environment is also a major contributor to the context of that system.
Those parts of the outside world which do NOT significantly interact with the system are part of its universe. These can be physically very close
Notes: Difficulties are:- deciding on boundary and choosing elements of environment
Basis for system boundary is level of significance and relevance to purpose of system. Boundary encloses those components which make a clear contribution to achievement and have characteristics, properties, or attributes which are considered in assessing the behaviour of the system. Environment contains elements which influence how the system behaves but these elements are not directly considered in assessing the behaviour of the system

## Slide 67: What’s the System Here?
A system boundary is an artificial (a mental creation) but useful concept in Systems Thinking.
It provides a way of “bounding” or “scoping” the situation of interest. It helps decide what is inside and what is outside the system
System boundaries can be temporal (time related), logical (purpose), or geographical (physical)
The choice of what is and what is not the chosen system of interest depends upon the observer and their reason for examining that system
Defining what is and what is not part of the system of interest is not easy

## Slide 68: Using Boundaries
The “right” boundary for thinking about a situation rarely coincides with existing political or physical definitions
We invent boundaries in order to simplify and clarify a complex situation – to help decide “what’s in” and “what’s out”
Where we draw the boundary impacts both PURPOSE and CONTEXT
We should always reconsider the boundary for each situation whether new or old
We should also be prepared to change the boundary as our understanding grows. Sometimes we don’t fully know why we are investigating a situation! We “have a feeling” – and its only by exploring the situation as a system we begin to appreciate what needs to be done which in turn will define the boundary

## Slide 69: The Observer
The context of a system also depends on who’s looking at it
We see different things
When exploring a system’s context we need to take multiple perspectives to increase our understanding
4
3

## Slide 70
A key question when Systems Thinking is
What is the context?

## Slide 71: Systems are made up of subsystems and Systems are subsystems of bigger Systems
Whenever we look “inside” the chosen system of interest we see further smaller systems or subsystems
Whenever we look outside the chosen system of interest we see that it is part of a larger system
We can use this concept to manage complexity through the use of subsystems

## Slide 72: The context of a subsystem comes from the system it sits within
At any level It is the other systems outside the boundary of our system of interest that provide its context. These other systems will provide constraints (requirements) on our system of interest

## Slide 73: Subsystems and Information Hiding
The fact that any system is made up of subsystems is extremely useful in Systems Thinking.
By “hiding” the detail in sub-systems it provides a way of managing complexity
This “abstraction” of reality is very powerful – it allows complex situations to be explained in simple ways
The map of the London underground is a classic example of abstraction to make complexity understandable. The “real” map is just too complex to be of any use in navigating the system.

## Slide 74: Abstraction in Design
TV
Object
Converts a signal into light and sound
Purpose
Higher-Level
Purpose
Entertain User
Pleasure User
Highest-Level
Purpose
Level of abstraction
TV
Mobile Phone
Lap/desk Top
Tablet
Projector
Theater Play/show
Cinema/Film
Sport

## Slide 75
A key question when Systems Thinking is
What’s inside?
What’s Outside?

## Slide 76: System Behaviour and Connections
Many Systems (particularly Business and Engineering Systems) are often concerned with a transformation – converting inputs to outputs. How the output varies over time is called the system behaviour
The behaviour of a system manifests itself in two related ways:
  Events are things that happen at a certain point in time. Events are the output of a system moment by moment. For example a commercial aircraft retracting its undercarriage can be treated as an event, so can a road traffic accident or the purchase of a new business unit.
  Patterns are an accumulation of events that display a recurring trend over time. For example a commercial aircraft pushes off from the stand, taxis, accelerates down the runway, rotates, becomes airborne, retracts its undercarriage, etc. in a series of events that defines a pattern of behaviour repeated by most commercial aircraft.
System
Outputs
Inputs
All systems will display patterns of behaviour if we observe them for long enough.

## Slide 77: Events, Patterns and Behaviour
Humans find events more memorable and often view reality just in terms of events. If you were involved in a road traffic accident – you might call the local police and exchange driver details. Indeed, it’s our ability to react to events that has ensured our survival!
Patterns or “trends” over time offer a deeper understanding of reality. It’s our ability to spot patterns that has lifted us from “just surviving” – but whereas reacting to events is instinctive, finding patterns is not! Reducing road traffic accidents at the pattern level could involve finding accident “hot spots” in terms of location and time and staffing the emergency services accordingly
BUT something is behind, or causing, the patterns – the System Structure
An accident hot spot

## Slide 78: Interrelationships, Structure and Behaviour
To fully understand a system we need to examine its behaviour over time. This behaviour can be simple, complex, desirable or undesirable but it is due to how the system components are interrelated – the system structure, organization or architecture
Because “Structure” is defined by the interrelationships of a system’s components, and not the components themselves, the structure is invisible
It is by changing the structure or organization of a system that we can significantly affect its behaviour
Events
Patterns
Structure, Architecture, Organization
We experience and remember events
Behind every event is a pattern
It is the interrelationships in a system that cause the patterns and events

## Slide 79: Change the Structure – the Systems Intervention
What could we do to reduce or remove this accident hot spot?
Ideas?
Side road speed limit 30
Main road speed limit 60
Accident hot spot
Reacting to events and patterns can make a difference but the real differences come with changes in the structure of the system

## Slide 80: Exercise
Same people who did the “Helium” tube exercise
Organize yourselves into two equal groups
Each group should form a “star” with their fingers touching
Keeping the finger in constant contact with underside of the tube lower it to the ground
Time 2 minutes

## Slide 81: Behaviour, Interrelationship and Feedback
The behaviour we observe in every system – designed or evolved is a consequence of the interrelationships between the components
Remarkably the dynamic nature of these interrelationships comprise just two forms (for the whole universe!!):
  Reinforcing feedback
  Balancing feedback
The behaviour of every system is due to these two forms of feedback and synchronisation of the feedback

## Slide 82: Properties and Characteristics of Systems Dynamic Behaviour and Feedback
Reinforcing (positive) Feedback: successive changes add to previous changes in the same direction
Date | Whole Price Index | 
July 1914 | 1.0 | 
January 1919 | 2.6 | 
July 1919 | 3.4 | 
January 1920 | 12.6 | 
January 1921 | 14.4 | 
July 1921 | 14.3 | 
January 1922 | 36.7 | 
July 1922 | 100.6 | 
January 1923 | 2,785 | 
July 1923 | 194,000 | 
November 1923 | 726,000,000,000 | 
German wholesale price index |  | The exponential growth of positive feedback
This model of “inflation” is a pure positive feedback loop which if left unchecked will lead to exponential growth – what economists call hyper-inflation. In this case undesirable – but such feedback can be beneficial

## Slide 83: Negative and Positive Feedback
Balancing (negative) Feedback: resists change in one direction by producing change in the opposite direction
Balancing feedbacks stabilise behaviour - they calm things down
In this economic example the full lines represent positive or reinforcing feedback, while the dotted lines represent balancing or negative feedback

## Slide 84: Behaviour is Affected by all the Elements in a System
This is the model developed by Keynes. He was able to “see” further connections and feedback loops in the bigger system. We often find that a lower level system is subject to feedback at a higher level.
The model given here is of course a qualitative model. But is does help in understanding the behaviour of a complex situation like a national economy.

## Slide 85: Properties and Characteristics of Systems System Stability
Imagine a ball, that was originally resting in the bottom of a bowl, moved up one side and released – it will eventually return to the bottom of the bowl
If the ball is on a flat surface then if it is moved it will stay in its new position
If a ball placed on an upside down bowl is disturbed it will move away from its original position
Stable
A system that is initially in equilibrium is disturbed, it is said to be stable if it returns to that equilibrium condition.
Unstable
A system that is initially in equilibrium is disturbed, it is said to be unstable if it continues to move away from equilibrium condition.
Marginally Stable
A system that is initially in equilibrium is disturbed, it is said to be marginally stable if it finds a new equilibrium condition.
Unstable systems can offer significant performance improvements but they can also destroy themselves
Date | Whole Price Index
July 1914 | 1.0
January 1919 | 2.6
July 1919 | 3.4
January 1920 | 12.6
January 1921 | 14.4
July 1921 | 14.3
January 1922 | 36.7
July 1922 | 100.6
January 1923 | 2,785
July 1923 | 194,000
November 1923 | 726,000,000,000
German wholesale price index | 

## Slide 86: System Stability
System Stability is determined by the interconnectedness and synchronization of the system elements
System Stability can be changed by increasing or decreasing (removing or adding) “connections”
  A stable system can be made less stable by reducing/removing balancing feedback or by increasing/adding positive feedback
  An unstable system can be made more stable by reducing/removing positive feedback or increasing/adding balancing feedback
System Stability can be changed by increasing or shortening the delays in a system – this is often counter intuitive.
Motorway Queues experience shock waves: fast-slow and stop-start behaviour because of an increase in the volume of vehicles causing a positive feedback. If we reduce the number of vehicles (reduce the positive feedback) the problem goes away!
The stop-start behaviour can also be influenced by introducing negative feedback into the system – variable speed limits. It should also be possible to change the behaviour by changing some of the delays in the system.

## Slide 87: Systems Thinking in Engineering
Utilises Systems Thinking to
  Understand context and purpose
    To elicit and analyse requirements
    To generate and explore solutions through abstraction
  Manage complexity
    Through determination of sub-systems
    Through multiple perspectives
  Manage emergent behaviour
    By paying attention to the “connections” between sub-systems
    By consideration of a lifecycle view
Putting it in to practice requires a systematic and repeatable approach – we need a process.
  The Systems Engineering Process is based on two fundamental basic processes:
    Divergent and Convergent Thinking
    Plan-Do-Check-Act
Notes: Text to go with this
Systems Engineering is a key enabler of effective pre-work – if you have the wrong requirements then you will get the wrong solution – regardless of how good your design (rest of engineering) is. At also you will discover this very very late in programme (in service, sales etc.)
Systems engineering Utilises a systems approach to understand context and purpose (which we will explain further later)
Systems engineering Is used to control emergence (simplistically to minimise unwanted / undesirable emergence, and to maximise / optimise the desired emergent properties – but to do this you need to understand the principle of emergence
Employs Systems Thinking to
  Enable elicitation and understanding of requirements – expressed in solution neutral form
  Use of requirements to create solutions – avoiding the natural jump to solution
  Flow down of requirements from one solution level to the next level of detail – utilising the understanding of functionality, decomposition of solution into architecture etc.
Provides key link to planning and risk identification based on understanding of requirements – gives you an idea of the iteration and areas needing special attention. Also – as you get requirements tells you what “evidence” you need to prove the requirements have been met – so drives the definition of the verification plan

## Slide 88: Divergent-Convergent Thinking a Systems Meta Process
Divergent Thinking
Convergent Thinking
Concerned with generating ideas or information about a situation or problem
Concerned with organizing and making sense of ideas or information
When attempting to understand a situation or solve a problem the task is to find amongst all the possibilities the critical aspects. This task logically comprises two activities:
    Generating information
    Organizing information
We often try to do this in one step by “jumping” to the “answer” – the problem is we stop thinking once we find a first adequate “answer”
It is better to divide the task up into its component activities

## Slide 89: Plan Do Check Act a Systems Meta Process
Plan
What has to be done
Do
Carry out the activity
Check
Check the activity
Act
Act on the check
Often attributed to the American quality guru Edwards Deming, he said he got the idea from Walter Shewhart the inventor of Statistical Process Control. But even Shewhart’s work can be traced to the Englishman Francis Bacon who first expounded the scientific method of Hypothesis, Experiment and Evaluation.
PDCA is logical common sense that is often not followed..
P
A
C
D
Notes: References:
Deming, W. Edwards (1986). Out of the Crisis. MIT Press. ISBN 0-911379-01-0.
Shewhart, Walter A[ndrew]. (1931). Economic control of quality of manufactured product. New York: D. Van Nostrand Company, ISBN 0-87389-076-0

## Slide 90: Systems Engineering uses a Systems Approach to System Design
Do
SYSTEM PROBLEM
UNDERSTAND
PROBLEM
“best”
solution
Stakeholder needs and expectations
Understand the problem in terms of Purpose and Context
solution
solution
solution
solution
Identify and document all possible solutions to the problem (Divergent Thinking)
Search and evaluate the solutions to determine and select the “best” solution
(Convergent Thinking)
Tailor the process, select the tools and determine the best checking strategy
Plan
GENERATE SOLUTION OPTIONS AND SELECT
Check (& Act)
Confirm that the selected solution solves the stakeholders’ problem
Confirm the understanding of the problem reflects the stakeholder’s needs and expectations
Check (& Act)
Check (& Act)
Confirm that the built System solves the stakeholders’ problem
Do
Do
MAKE THE SYSTEM TO THE DESIGN
Built System

## Slide 91: How do we Handle Complexity in System Design?
The complexity of the proposed system means it will have to be DESIGNED in “bite” sized chunks
We start by designing the SYSTEM as a number of subsystems – i.e. what is the architecture and technology of the system
System
Subsystem 1
Subsystem 3
Subsystem 2
We then design the SUBSYSTEMS as a number of lower level elements, ultimately down to…
The design of individual COMPONENTS
Component 2.1
Component 2.2
From the system design we have the necessary sub-purpose and context to specify the Subsystem Requirements
From the subsystem design we have the necessary context to specify the Component Requirements
In order to successfully design the system – Systems Thinking tells us we need to know its purpose and context
In order to design the subsystems, Systems Thinking tells us we need to know the purpose and context for each subsystem. This can only be known if we have designed the system

## Slide 92: How do we Handle Complexity in System Design?
The complexity of the proposed system means it will have to be DESIGNED in “bite” sized chunks
We start by designing the SYSTEM as a number of subsystems – i.e. what is the architecture and technology of the system
System
Subsystem 1
Subsystem 3
Subsystem 2
We then design the SUBSYSTEMS as a number of lower level elements, ultimately down to…
The design of individual COMPONENTS
Component 2.1
Component 2.2
From the system design we have the necessary sub-purpose and context to specify the Subsystem Requirements
From the subsystem design we have the necessary context to specify the Component Requirements
In order to successfully design the system – Systems Thinking tells us we need to know its purpose and context
In order to design the subsystems, Systems Thinking tells us we need to know the purpose and context for each subsystem. This can only be known if we have designed the system

## Slide 93: How do we Handle Complexity in System Build?
The complexity of the proposed system means it will have to be BUILT in “bite” sized chunks
We start by designing the SYSTEM as a number of subsystems – i.e. what is the architecture and technology of the system
System
Subsystem 1
Subsystem 3
Subsystem 2
We then design the SUBSYSTEMS as a number of lower level elements, ultimately down to…
The design of individual COMPONENTS
Component 2.1
Component 2.2
From the system design we have the necessary sub-purpose and context to specify the Subsystem Requirements
From the subsystem design we have the necessary context to specify the Component Requirements
These Components once realised will be integrated to build Subsystems
The Subsystems will be integrated to build the System
The Built System

## Slide 94: The V Diagram
Design
System
Design
Subsystems
Build and Check Subsystems
Build and Check System
Design
Components
Build and Check Components
Realise
Components
Subsystem Level
Component Level
System Level
Stakeholder
Requirements
Subsystem
Requirements
Component
Requirements
Built and Checked Components
Built and Checked Subsystems
Working
System
Component
Build and Check Requirements
System Build And Check Requirements
Subsystem Build and Check Requirements
We have to check at every level. The lower-level checks supporting the higher levels
To manage complexity we design in levels

## Slide 95: Systems Engineering is Fractal
System
(Current Level)
Requirements
Subsystem
(Lower Level)
Requirements
Built and Checked (Lower Levels)
Subsystems
Working
(Current Level)
System
Engineer
Subsystems
(Lower Levels)
Design System
(Current Level)
Build and Check System
(Current level)
System
Build and Check Requirements
At any one Level there is a
Fundamental Process – The Process Is Recursive

## Slide 96: Systems Engineering is Fractal
System
(Current Level)
Requirements
Subsystem
(Lower Level)
Requirements
Built and Checked (Lower Levels)
Subsystems
Working
(Current Level)
System
Engineer
Subsystems
(Lower Levels)
Design System
(Current Level)
Build and Check System
(Current level)
System
Build and Check Requirements
At any one Level there is a
Fundamental Process – The Process Is Recursive

## Slide 97: The Design System Process
Determine System Requirements
Create System Design Concept
Design System
Verify & Validate System Design
Stakeholder
Requirements
System
Design
System
Design
Subsystem
Requirements
Build and Check Requirements
Design System
Understand the problem – what does the customer want in measurable terms?
Make the system concept as good as it can be – do we have the robust optimum?
Verify and Validate the system design
A second key output” are the Build and Check Requirements
A key output is the Subsystem Requirements
What are the design choices and what system concept will best meet the requirements?

## Slide 98: Systems Engineering is Fractal
System
(Current Level)
Requirements
Subsystem
(Lower Level)
Requirements
Built and Checked (Lower Levels)
Subsystems
Working
(Current Level)
System
Engineer
Subsystems
(Lower Levels)
Design System
(Current Level)
Build and Check System
(Current level)
System
Build and Check Requirements
At any one Level there is a
Fundamental Process – The Process Is Recursive

## Slide 99: The Build and Check System Process
Accept (Validate) System
Check (Verify) the built System
Build System
Physically build the System from the Subsystems
Demonstrate that the system meets the pre-determined and agreed acceptance criteria
Built and Checked
Subsystems
Working
System
Build and Check
Requirements
Check and Accept Evidence
Check that the system has been built correctly against pre-determined verification criteria and methods
Build and Check System
A key output is the evidence that the right system has been designed and built correctly

## Slide 100: The Output of Systems Engineering
It is important to note that the output of Systems Engineering is
Indeed you can argue that the purpose of Systems Engineering is to generate information about the system being created such that it can be successfully built
INFORMATION

## Slide 101: Checking
Checking as we Build
As the components are put together to make subsystems, and subsystems put together to make the system, common sense dictates that we check what has been built at each stage, that is:
  Components and subsystems meet their requirements
  The system behaves as expected by the customer
Both are necessary to have complete confidence in the final system
Checking here is obviously the correct thing to do – BUT it could be too late!

## Slide 102: Verify and Validate Across the V
Years
Subsystem Level

## Slide 103: By Checking we Mean Verification and Validation (V&V)
Verification: Confirmation by examination and provision of objective evidence that the specified requirements to which an end system is built, coded or assembled have been fulfilled
Validation: Confirmation by examination and provision of objective evidence that the specified intended use of an end system or aggregation of end systems is accomplished in an intended usage environment
Did we do the thing right?
Did we do the right thing?
These are the generally accepted systems engineering definitions of V&V. The implications of these are quite profound since Validation becomes “something that can only be done when the thing is built! However, it is important to realise validation can apply throughout the system design activity.
Notes: The terms “Verification” and “Validation” are often confused, mis-used and misunderstood. These definitions reflect the generally accepted meanings for these terms.
Verification is a free-standing black box process which establishes that an item meets the requirements established for it, i.e., “Did we build the thing right?”.
Validation is a higher order process which establishes that an item meets the end purpose of that item, i.e. “Did we build the right thing?”
Arguably, a subsystem at a particular tier has an end use in the tier above. When tested within its own tier, this is, in the context of the above definitions, “Verification”. When it is integrated into the tier above, and shown to operate correctly (as distinct from simply satisfying its “shalls”), this could be viewed as “Validation”; although the term is seldom used in this context, the activity is implicit in the integration testing that occurs at that tier.
But the discussion is somewhat specious – in practice, the term “Validation”, when used in accordance with these definitions, is generally only commonly used to refer to the Operational Test and Evaluation process which the DoD typically undertakes at Tier 0, following delivery of the system – and in that context it is precisely correct. But most commonly, the term is lumped with its partner into the generic “V&V” which is even more widely mis-used than the term “system”.

## Slide 104: Checking
Checking as we Design
As system elements are designed common sense dictates that we check as we progress that the
  requirements are correct - are we designing the right system? (Validation)
  design meets the requirements - has the system been designed right? (Verification)
Both are necessary to have complete confidence in the final system
We need to check as we progress

## Slide 105: Verify and Validate Inside the V

## Slide 106: Checking by Review
Why
  It is business critical that any project remains on track and at each stage fulfils the specified requirements.
  Reviews at specified stages of the lifecycle ensure that all the business and functional requirements fully comply with their agreed specifications.
  Reviews are essential to reduce risk - experts are used to independently assess the status of the project.
Generic Review Principles
  Reviews held in accordance with current engineering plan even if project is late
  Review uses existing project documents where possible
  Reviews are objective
  Reviews are evidence-based
  Reviews are conducted by acknowledged “expert” assessors
  Review Chair is independent of the project
  Results reported to the project director
  Reviews referred to by numbers, e.g. 2
  Reviews are key learning points - a basis for corporate learning
But WHEN do we Review?

## Slide 107
Systems Engineering operates in two dimensions
Complexity
Lifecycle

## Slide 108: Generic Lifecycle
conceive
design
build
deliver
support
decommission
Next project
Time
design
build
conceive
decom-
mission
THE LIFECYCLE
deliver
support
Lifecycle Principles
  Through Life Capability Principles
  Project and Technical Engineering Activity in Distinct Phases in a Cycle
  Depicting the Cycle Linearly with Time describes a Lifecycle
  Systems Engineering Principles and Processes Can Be Applied

## Slide 109: Some Systems Engineering Lifecycles
IG
MG
MOD CADMID Lifecycle
Concept
Assessment
Demonstration
Manufacture
In-Service
Disposal
US DoD Acquisition Lifecycle
R
U
P
D
C
S
Concept
Development
Production
Utilisation & Support
Retirement
ISO 15288 Lifecycle Phases
They all align to ISO 15288

## Slide 110: In Waters
Notes: Animated – Mention additional supporting notes in pack
The lifecycle of a product. From cradle to grave (or lust to dust!).
Firstly, for a product, there is a lifecycle that is divided-up into stages. This covers the period of activity from the twinkle in the designer’s eye, through to the removal of the product from service, and the associated activities to remove any legacy of hardware, tooling, contractual obligations, etc. The timescale of the lifecycle can vary from 10 to 50 years, dependent on the product and market.
Secondly, during this period of time, there are some significant milestones to be achieved
Thirdly, there are some review points that are aligned to these milestones, in order to check that the required activities are being completed
[The next slides in the handouts identify the STAGE descriptions]

## Slide 111: They all fit 15288
R
U
P
D
C
S
Concept
Development
Production
Utilisation & Support
Retirement
ISO 15288 Lifecycle Phases

## Slide 112
R
U
P
D
C
S
Lifecycle Activity – Lifecycles within Lifecycles
System-Level
R
U
P
D
C
S
Application Level
If delivering an integrated capability, for example, MS , Chemistry and Application Systems, these different elements of the system of systems may need to be at a higher level of maturity earlier than the main system

## Slide 113: Lifecycle and the V-Diagram
Notes: Animated – Mention additional supporting notes in pack
The lifecycle of a product. From cradle to grave (or lust to dust!).
Firstly, for a product, there is a lifecycle that is divided-up into stages. This covers the period of activity from the twinkle in the designer’s eye, through to the removal of the product from service, and the associated activities to remove any legacy of hardware, tooling, contractual obligations, etc. The timescale of the lifecycle can vary from 10 to 50 years, dependent on the product and market.
Secondly, during this period of time, there are some significant milestones to be achieved
Thirdly, there are some review points that are aligned to these milestones, in order to check that the required activities are being completed
[The next slides in the handouts identify the STAGE descriptions]

## Slide 114: More Than a Process
PROCESS
PEOPLE
TOOLS

## Slide 115: Exercise: People
Capital Cities
  Part 1: individually, list as many Capital Cities of the world as you can in two minutes
  Part 2: in small teams, use your individual lists to create a team list – time five minutes
Notes: THE RECKONING
•
Review the answer sheet.
•
Give yourself one point for each correct individual answer.
•
Score the group answer.
•
Complete the following chart
Gp A
Gp B
Gp C
Gp D
Gp E
Best Individual Score:
Lowest Individual Score:
Average Individual Score:
Group Score:
Bush (snr & jnr), Clinton, Reagan, Nixon, Lincoln, Roosevelt, Johnson, Ford, Carter
Washington, Eisenhower, Adams, Kennedy...

## Slide 116: Sharing Knowledge
Extent of
my knowledge
Gaps in my knowledge
Team knowledge is greater and fills the gaps

## Slide 117: Creating Knowledge
Working as a team will cause us to share knowledge but
  System Design often requires us to be creative
We can be individually creative, BUT we are better when we work as a team
  Voicing my ideas can help other team members to be more creative and vice versa

## Slide 118: People and Tools in Systems Engineering
PEOPLE
Systems Engineering is a team sport!
People are essential - they generate the information required
Teams are better than individuals because of
  the sharing of knowledge and expertise
  the information and knowledge generated by working together
System design and development can involve many disciplines. Hence for complex multidisciplinary systems we have to have highly skilled multidisciplinary teams
For a multidisciplinary team to deliver they must be able to communicate with each other to share information and have a common understanding to avoid having different perceptions
TOOLS
Processes tell you what to do and when to do it (may also say who does it) – they should NOT specify how to do it – this is the job of tools
BUT we need a set of tools that all teams members can use, with confidence, that allow us to handle the complexity of the system but at the same time are simple enough for the whole team to use – we need generalist systems tools
Systems Engineering Tools are primarily communication devices that allow different disciplines to explore systems issues, often by building abstract models. They are scalable (any size of system), universal (any type of system)and above all simple (anybody can use them)

## Slide 119: Systems Tools Build Models to Help the Team Reach a Common Understanding
Systems Engineering makes great use of MODELS to look for structures, relationships and dependencies at an abstract level to help predict behaviour at the real level

## Slide 120: Determine System Requirements
Requirements Database
Stakeholder Map
Determine system stakeholders and select key ones for requirements elicitation
Tree Diagram/Analytic Hierarchy Process
Organize and prioritise key stakeholder requirements
The User Requirements defines the expressed requirements of a particular stakeholder or stakeholders
Affinity Diagram
Elicit and capture key stakeholder requirements
Captures how a user expects to interact with a system
Use Case
The Business Requirements provide the rationale and overall business constraints for a system development project
Gather Requirements
Identifies and explores system solutions at different levels to determine System Meta-Solution
Need Mean Analysis
Analyses expressed requirements into their atomic form to identify and clarify missing and ambiguous requirements
Systemic Textual Analysis
Generates and organizes system generic functionality necessary to achieve the Operational Requirement
Viewpoint/Functional Analysis
Captures and shows how the component functionality of a system must cooperate to deliver the Operational Requirement
Function Flow Diagram
Determine the necessary generic System Functionality
Captures the potential functional failure modes, effects and causes to identify remedies ab initio
Functional Failure Mode and Effect Analysis
Identifies causal paths for potential system sensitivities
Flow Sensitivity Analysis
Determine the Emergent Functionality
Cross checks requirements for consistency and completeness
Quality Function Deployment 1
Analyse and Validate Requirements
Specify
Requirements
Determine Validation and Verification methods for each requirement and specify V& V Requirements
Verification Compliance Matrix
The System Requirements defines the measurable design requirements for the system

## Slide 121: Create System Design Concept & Design System
Determine the factors that are most likely to influence the robustness of a nominal design
Design 2 Noise Matrix
Identifies and captures the factors that influence the performance of a system output
Parameter Diagram
Qualitative Robustness and Critical Parameter Analysis
Identify and document the potential failure modes, Effects and Causes
Design Failure Mode and
Effects Analysis
Use models or physical Designed Experiments to characterise the transfer function and thereby robustness of the system design.
Quantitative Robustness Analysis
Designed of Experiments
Simulation and Modelling
Parameter & Tolerance Design
Update QFD 2 with the design parameter target values and as appropriate - tolerances
Quality Function Deployment 2`
Update System Definition and Sub-System Requirements and associated Sub-System Verification Requirements
Requirements Database
Determines the natural structure of a system that can be exploited
N2 Analysis
Determines candidate system architectures with minimal interfaces
Logical System Architecting
Identifies and captures all possible functional solutions to a system design problem and thereby determine suitable candidate system concepts
Function Means Analysis
Compares candidate system concepts against a set of criteria
Pugh Matrix
Verify System Concept Solution meets the System Requirements and allocation of Sub-System Requirements
Quality Function Deployment 2
Use Engineering Modelling, Simulation and Analysis to undertake preliminary design and feasibility
Preliminary Design and Feasibility
Create Candidate System Concepts
Create System Definition and Sub-System Requirements and associated Sub-System Verification Requirements
Requirements Database
Use quantitative models to explore solution space to find robust optimum and thereby determine design parameter settings and tolerances

## Slide 122: Verify and Validate System
Reliability Block Diagram
Model System Failures as a Fault Tree
Fault Tree Analysis
Model the system design to predict the system reliability
Realisation System Modelling and Analysis
Identifies sequence of logical process steps (functions) of the realisation system
Sequence Diagram
Identify and document the potential failure modes, Effects and Causes
Process Failure Mode and
Effects Analysis
Update Verification Compliance Matrix
Verification Compliance Matrix
Assess supportability through predicted
reliability and operational analysis
Supportability Assessment
Understand the System Operation
Operational Analysis
Check that System Concept Solution is realizable and determine critical realization parameters and target values
Quality Function Deployment 3
For the critical realization parameters determine the Assurance Requirements and target values
Quality Function Deployment 4
Perform Verification Activities and collect verification evidence
Collect Verification Evidence
Design and perform tests
Requirements Database
Identifies and captures the factors that influence the performance of a system output
Parameter Diagram

## Slide 123: A Fool With a Tool
Is a More Dangerous Fool
Give somebody a hammer and they’ll find things to hit with it!

## Slide 124: This Section:
Explained why Systems Engineering is necessary
  Undesirable emergent behaviour as a consequence of complexity
Explained the relationship between Systems Thinking, Systems Approaches and Systems Engineering
Introduced Systems Thinking as the foundation of Systems Engineering
Provided an overview of Systems Thinking
  The only way to manage complexity
Showed how Systems Engineering utilises Systems Thinking to
  Understand context and purpose
  Manage complexity
  Manage emergent behaviour
Introduced the three ingredients of Systems Engineering
  Process (Lifecycle and Complexity)
  People (multidisciplinary teams)
  Tools (easy to use, scalable and universal)

## Slide 125: This Course Will Focus on
Determine System Requirements
Create System Design Concept
Design System
Verify & Validate System Design
Stakeholder
Requirements
System
Design
System
Design
Subsystem
Requirements
Build and Check Requirements
Design System

## Slide 126: The V Diagram of Systems Engineering
Design
System
Design
Subsystems
Build and Check Subsystems
Build and Check System
Design
Components
Build and Check Components
Realise
Components
Subsystem Level
Component Level
System Level
Stakeholder
Requirements
Subsystem
Requirements
Component
Requirements
Built and Checked Components
Built and Checked Subsystems
Working
System
Component
Build and Check Requirements
System Build And Check Requirements
Subsystem Build and Check Requirements

## Slide 127: V Diagram of Agile (a Version)
This can be done “better” by Systems Engineering

## Slide 128: The Process
Systems Engineering is more customer focused! It’s just a matter of doing the checks correctly

## Slide 129: Compare and Contrast
The Agile Manifesto is based on twelve principles: | The SE manifesto is based on
Customer satisfaction by early and continuous delivery of valuable software Welcome changing requirements, even in late development Working software is delivered frequently (weeks rather than months) Close, daily cooperation between business people and developers Projects are built around motivated individuals, who should be trusted Face-to-face conversation is the best form of communication (co-location) Working software is the principal measure of progress Sustainable development, able to maintain a constant pace Continuous attention to technical excellence and good design Simplicity—the art of maximizing the amount of work not done—is essential Best architectures, requirements, and designs emerge from self-organizing teams Regularly, the team reflects on how to become more effective, and adjusts accordingly | Moto: To listen, to understand, to deliver 1 To satisfy all stakeholders by the timely delivery of capability 2 To embrace all requirement changes 3 To deliver solution options at the correct time for consideration and agreement 4 To maintain close daily cooperation between all pertinent stakeholders and system developers 5 To build programme and projects around enthusiastic, motivated and capable teams 6 To interact will all stakeholders face to face through conversation and diagrams as the ultimate form of communication 7 To measure performance through evidence-0based demonstrable capability 8 To smooth the work-flow 9 To explore all choices to ensure excellent design 10 To simplify through understanding 11 To share at all times 12 To reflect and review continuously 13 To identify and rectify potential issues before they are real