## Slide 1: A Systems Approach to Determine System Requirements
This Session
Defines a Systems Approach to Determining Systems Requirements
Introduces the Holistic Requirements Model – a systems approach to understanding requirements
Demonstrates the importance of system functionality as an invariant and logically defensible method of handling complexity

## Slide 2: Where are we? And what are we trying to do?
Purpose :
  To elicit, capture, identify and interpret customer, and other stakeholder, requirements accurately, and to translate these into clear, concise, complete, consistent and confirmable technical system design requirements
Outcomes :
  A set of source requirements that define the customer and stakeholder needs and expectations (especially those aspects that are Critical or Key Requirements )
  A complete and consistent set of measurable system design requirements that have been validated and verified as satisfying the customer and stakeholder requirements

## Slide 3: Determine Requirements: Tasks and Tools
Notes: 9
9

## Slide 4: Understanding Requirements
Requirements originate from various sources
Source requirements are:
  Incomplete
  Inconsistent
  Incorrect
  Ambiguous
  Rambling
  Unconfirmable

## Slide 5: Incomplete
*

## Slide 6
*

## Slide 7: Inconsistent

## Slide 8: Incorrect

## Slide 9: Ambiguity of Understanding
“Aoccdrnig to a rscheearch at Cmabrigde Uinervtisy, it deosn't mttaer in waht oredr the ltteers in a wrod are, the olny iprmoatnt tihng is taht the frist and lsat ltteer be at the rghit pclae. The rset can be a toatl mses and you can sitll raed it wouthit porbelm. Tihs is bcuseae the huamn mnid deos not raed ervey lteter by istlef, but the wrod as a wlohe.”

## Slide 10: Ambiguity of Context

## Slide 11: Un-confirmable
The System should be easy to use

## Slide 12: Getting to Grips with Requirements
Achieving
  Completeness: requires several viewpoints to be taken
  Consistency, Conciseness and Clarity: requires the identification and removal of ambiguity this in turn requires communication to share information and arrive at a common understanding - to avoid having different perceptions
  Correctness and Confirmation: requires the verification and validation of requirements
This demands discipline and organization
A consistent approach to engineering the requirements – a process (high level shown earlier)
A consistent way of organizing and interpreting requirements – a requirement model or architecture

## Slide 13: Organizing Requirements
  Operational Requirements
  Functional Requirements
  Non-functional Requirements
          Non-functional Performance Requirements
          Non-functional System Requirements
          Non-functional Implementation Requirements
There are many ways of organizing requirements, but only one systems view. This systems view of requirements provides a complete and consistent framework for organizing and understanding the deficiencies of a set of requirements.
It is called the Holistic Requirements Model and says that a complete and consistent set of system requirements will comprise:
Notes: 11

## Slide 14: Operational Requirements
An Operational Requirement defines the major purpose of a system (i.e. what it fundamentally does - its capability) together with the key overarching constraints (that define the context)
System
Operational Requirement
Dishwasher
To clean domestic eating and cooking utensils and crockery efficiently and without damage
Civil Aircraft
To transfer passengers and their baggage from one point to another efficiently and safely
Toaster
Overhaul
Aircraft
To achieve high aircraft availability in a cost
-effective and safe fashion
p.s. customers often don’t tell us their Operational Requirement
All systems have a purpose and a context. The job of the Operational Requirement is to define these in simple terms - to define the “mission” of the system
All Systems have purpose and context – the Operational Requirement captures these

## Slide 15: 1961: Kennedy and the Ultimate Operational Requirement
President John F Kennedy in a speech to a joint session of Congress broadcast on TV and radio around the United States
“I believe that this nation should commit itself to achieving the goal,
  before this decade is out, of landing a man on the Moon and returning him safely to Earth”
One
Small
Step
Writing an Operational Requirement is not easy. It can take several hours to arrive at an agreed set of 20 or fewer words!
Do you know the Operational Requirement of the system you are currently working on?
Is it written down in 20 or fewer words that is the common understanding of the whole team?

## Slide 16: Functional Requirements
Functional Requirements specify the functions of the system - what the system has to DO in order to satisfy its Operational Requirement
For example some of the functions of a civil aircraft are:
  Navigate aircraft
  Manoeuvre aircraft
  Store passengers
  Control passenger storage environment
  Communicate with other aircraft and ATC
  Etc.
Note that a Functional Requirement contains a function expressed as a phrase comprising a verb (action) followed by a noun (object)
  A functional requirement should define something the system has to DO
  A phrase can have a verb but not be a function! For example “easy to use” has a verb but this is not a function – we don’t say the system “does easy to use” it has “to be easy to use” – a property or attribute
  Best practice is to define functions as verb noun combinations that describe an action on an object
  Beware of pseudo-functions, verb noun combinations that do not define an action on an object. For example ”provide style” is a pseudo-function because style is a property and not a thing – it is an abstract noun rather than a common noun. Functions that end with an abstract noun are pseudo-functions
We try to write Functional Requirements in way that does not specify, imply or assume a solution (like seat passengers). However, every system has to integrate with legacy systems and therefore this is not always possible
Notes: 13

## Slide 17: Non-functional Requirements
Non-functional requirements do NOT specify what the system has to do (but they might imply it!)
Non-functional requirements specify:
  How well it does something
  How it does something
They fall into three categories:
  Non-functional Performance
  Non-functional System
  Non-functional Implementation
Non-functional Requirements are constraints on the system
Notes: 14

## Slide 18: Non-functional Performance Requirements
Non-functional Performance Requirements are linked to functions and define how well a particular function has to perform – they are the constraints on a particular function. They comprise an attribute or property with an associated target value
Function
Non-functional
Performance Requirement
Navigate
aircraft
System
Aircraft
There is no verb! Hence these are not functional requirements (they do, however, IMPLY a Functional Requirement)

## Slide 19: Non-functional System Requirements
Non-functional System Requirements define constraints that affect the whole system (at least more than one function) and include:
  Physical Attributes
    System Size
    System Weight
    etc.
  The ilities
    System Reliability
    System Maintainability
    System Interoperability
    etc.
  System Performance
    System Cost
    System Speed
    System Manoeuvrability
    etc.
Note: the Non-functional System Requirements will get “flowed down” in to lower level requirements
Performance Requirements come in two forms: those that affect the system
and those that affect
a specific function
WE DELIBERATELY SEPARATE THEM
Notes: 16

## Slide 20: Non-functional Implementation Requirements
Non-functional Implementation Requirements define how a system is to be built in terms of a specific technology. They are solution-based requirements from the customer or legislation
Function
Non-functional
Implementation Requirement
Communicate ..
Phillips A/C 1267 VHF Radio
System
Aircraft
Remove Waste
Electric Pump
Dishwasher
Receive Power
UK Domestic 13A Plug to BS1363
Toaster
Overhaul
Aircraft
Maintain Component History
Microsoft Access database on a PC
Non-functional Implementation Requirements come in two types: Justifiable: where the requirement is reasonable - typically because it relates to a design decision made at the higher system level
Lazy: where the stakeholder has resorted to a solution-based requirement because they do not know how to express it otherwise
We need to identify the Non-functional Implementation Requirements and determine whether they are lazy or justifiable

## Slide 21: Summary: The Holistic Cutting of the Cake!
Holistic Requirements Model
The requirement categories of the Holistic Requirements Model are not arbitrary – together they form a complete and consistent set of requirements that has a structure which we can exploit to identify missing requirements and provide a powerful universal framework for system design

## Slide 22: Using the Holistic Requirements Model
The flowchart opposite can help in consistently and correctly categorizing a set of source requirements
Its use does require practise BUT it can provide a fast method to identify the deficiencies in a set of source requirements
Even experienced users will “get it wrong” on the first pass – but know subsequent iteration will address any miscategorization

## Slide 23: Exercise – Requirements Categories
In teams go through your toaster requirements and indicate which are:
  Operational requirements OP
  Functional requirements F
  Non-functional requirements
    System NFS
    Performance NFP
    Implementation NFI
Time 20 minutes

## Slide 24: Nature of Customer Requirements
Humans tend not to specify functionality!
It is assumed or implied through constraints
What is often missing from a set of requirements is the functionality
It’s not surprising, actually! Customers are often not interested in how something is done but how well it’s done
We must, however, determine has to be done - the functionality - because it is this that the system has do to deliver the customer’s expressed requirements

## Slide 25
What is the generic functionality necessary to
  “to toast bread product”
Time 10 minutes
To toast bread product
Toasting System
Notes: .

## Slide 26: Generic System Functionality
Generic System Function | Implementation
Load bread | Stick bread slice on end of toasting fork
Generate heat | Open coal fire
Apply heat | Use toasting fork to bring bread close to open fire
Monitor toasting | Look at the bread from time to time
Control toasting | Move bread to get even toasting
Remove heat | Use toasting fork to bring toast away from coal fire
Unload toast | Take toast off the toasting fork
Generic System Function | Implementation
Load bread | Put bread into slots
Generate heat | Electric elements
Apply heat | Lower bread next to elements using lever mechanism
Monitor toasting | Look at the bread from time to time
Control toasting | Timer
Remove heat | Lift bread from elements using lever mechanism
Unload toast | Take toast from slots

## Slide 27: Generic Toaster Functionality
Toast Bread Product
Load Bread
Monitor Toasting
Control Toasting
Remove Heat
Unload Toast
Apply Heat
Generate Heat
Did your requirements for the toaster specify any of these?
How do your requirements relate to the system functions?
System
Purpose
Sub-
Purpose
Every engineered system has an underlying set of functionality that enables it to achieve its purpose. Similar systems will have similar functionality; indeed, systems that have the same purpose will have a set of functionality that is identical. This functionality is the Generic System Functionality (GSF) and is time invariant (provided the purpose does not change the GSF does not change)
Whilst the GSF is a consequence of the system purpose and is fixed, it can be implemented in many ways which change as technologies evolve and emerge. The generic system functionality is not the complete set of system functionality – a system can have functionality that is not generic:

## Slide 28: Using Functionality to Manage Complexity
In Systems Engineering
Systems Engineering handles complexity by dividing the problem up into simpler yet integrated and interdependent sub-elements. It helps to be able to identify the sub-elements at an early stage, but how this is done is critical - the best way is to determine an invariant system architecture
Purpose ≡ Function
For a given problem (Operational Requirement) there will be a fixed set of generic functions that will not change over time. These generic functions provide a rational and invariant basis for the division of that problem

## Slide 29
I WANT
WOW!
The problem is getting from here to here
The Expressed Requirements are never complete, consistent, correct or clear
are just the
We have to find the unspoken requirements – but how?
The complexity of the problem and the likely complexity of the solution means it is difficult to consider the whole.
The approach has to be one of divide and rule. But what is the best way to divide?

## Slide 30: The Systems Approach to System Design
Requirements
-Land
Solution-Land
FUNCTIONALITY
The bridge between requirements and the solution is the functionality (purpose)
Functionality helps us uncover the unspoken requirements
Functionality is invariant and provides a consistent basis for dividing and ruling

## Slide 31: Functionality Delivers what the Customer Wants
Key = strong medium weak
◎
○
△
Even Toasting
Quick
Affordable
Easy to Use
Attractive
Reliable
etc
Load Bread
Monitor
Toasting
Control
Toasting
Remove Heat
Unload Toast
Apply
Heat
Generate Heat
Generic System Functions
What the customer wants

## Slide 32: Functionality Delivers what the Customer Wants
Key = strong medium weak
◎
○
△
Even Toasting
Quick
Affordable
Easy to Use
Attractive
Reliable
etc
Load Bread
Monitor
Toasting
Control
Toasting
Remove Heat
Unload Toast
Apply
Heat
Generate Heat
Generic System Functions
What the customer wants
○
○
○
○
○
○
○
○
○
○
○
◎
◎
◎
◎
◎
◎
◎
◎
△
△
△
△
△
△
△
△
△
△
△
△
△
△
△

## Slide 33: The Consequences
Thinking Functionally is the Pre-work that will reduce the Rework
Elicit and gather stakeholder requirements
Determine system concept
Build prototype and test
Redesign
Build prototype and test
Realise/Produce
The Traditional approach appears “faster” we have an answer quickly BUT!
Remember
Elicit and gather stakeholder requirements
Determine system concept
Build prototype and test
Realise/Produce
Determine System Functionality
The Systems Engineering approach is initially slower! But faster in the end
1st
Attempt
Elicit and gather stakeholder requirements
Determine system concept
Build prototype and test
Realise/Produce
Determine System Functionality
And it gets quicker every time!
2nd
Attempt

## Slide 34: Generic Functionality Helps Us Innovate: Automate Manual Functions
Generic System Function | Implementation
Load bread | Stick bread slice on end of toasting fork
Generate heat | Open coal fire
Apply heat | Use toasting fork to bring bread close to open fire
Monitor toasting | Look at the bread from time to time
Control toasting | Move bread to get even toasting
Remove heat | Use toasting fork to bring toast away from coal fire
Unload toast | Take toast off the toasting fork
Generic System Function | Implementation
Load bread | Put bread into slots
Generate heat | Electric elements
Apply heat | Lower bread next to elements using lever mechanism
Monitor toasting | Look at the bread from time to time
Control toasting | Timer
Remove heat | Lift bread from elements using lever mechanism
Unload toast | Take toast from slots
M
A
M
M
M
M
M
M
M
M
A/M
A/M
A/M
M
The next generation of toasters will aim to automate monitoring!

## Slide 35: Generic Functionality Helps Us Innovate: Expand the System Boundary
Generic System Function | Implementation
Load bread | Put bread into slots
Generate heat | Electric elements
Apply heat | Lower bread next to elements using lever mechanism
Monitor toasting | Look at the bread from time to time
Control toasting | Timer
Remove heat | Lift bread from elements using lever mechanism
Unload toast | Take toast from slots
Include external boundary functionality
Include external boundary functionality

## Slide 36: Generic Functionality helps us innovate: Explore functional solutions

## Slide 37: Discussion – Generate Heat - Solutions
What are all the solutions to the GENERATE HEAT function
Toasting System

## Slide 38: Generic Functionality helps us Create Holistic Solutions

## Slide 39: There is more to a system than its Generic Functionality
The generic system functionality is not the complete set of system functionality – a system can have functionality that is not generic:

## Slide 40: There is more to a system than its Generic Functionality
The generic system functionality is not the complete set of system functionality – a system can have functionality that is not generic:
  Solution Dependent Functionality: A particular generic function solution may require further solution specific functionality. For example Generate Heat can be solved by Electric Element but this solution demands that you “Earth Case” to protect the user
  Legislation Dependent Functionality: legislation requires us to incorporate additional functionality. For example electric toasters have to isolate electricity
  Architectural Functionality: At the system level the collected functional solutions require further functionality typically to support, align, contain and protect. These functions manifest as structures, casings, frameworks, chassis etc.
  Emergent Functionality: Functionality aimed at managing emergent behaviour/properties. Usually relates to informing the user of failure situations

## Slide 41: The First Toaster
The first complaints?

## Slide 42: Finally: Functions can be Modelled Mathematically
In certain cases it is possible to model the system mathematically
  Outputs(Y) = function(Inputs(U), State(X))
If we can model the system before it is built we can predict its behaviour – there are NO SURPRISES!
What limits us is our mathematical ability to handle uncertainty
Outputs (Y)
System (X)
Inputs (U)

## Slide 43: Traceability and Emergence
The System Functionality provides a way of flowing down requirements
Assess potential emergent behaviour through the transmission of variation

## Slide 44: The Systems Approach to System Design
Functionality helps us uncover the unspoken requirements
Functionality is invariant and provides a consistent basis for dividing and ruling
Requirements
-Land
Solution-Land
FUNCTIONALITY
The bridge between requirements and the solution is the functionality (purpose)
Functionality helps us determine the system architecture
Functionality helps us identify and select the technological solutions

## Slide 45: Holistic Requirements Model
The categories of requirements provide a complete and consistent framework that is driven by the Operational Requirements and has the Functional Requirements (what is to be done) at its heart
The Holistic Requirements Model allows us to “divide and rule” through using the functionality as the basis for work division

## Slide 46: Using The Holistic Requirements Model
Non-functional
Performance
Requirements
Infers
Functional Requirements
Non-functional
System
Requirements
Operational
Requirements
Non-functional
Implementation
Requirements
Infers
Demands
Requires
Requires
Infers
Requires
We can use the Holistic Requirements Model to deduce and infer
the requirements that have not been expressed by the customer

## Slide 47: Holistic Requirements Model: Not the Silver Bullet
The Holistic Requirements Model provides a sound framework for understanding requirements and indicating where they are deficient but to achieve this requires
Determine
System
Requirements
System
Design
Requirements
Clear
Concise
Complete
Consistent
Correct
Confirmable
PEOPLE
TOOLS
Stakeholder/
Source
Requirements
Ambiguous
Rambling
Incomplete
Inconsistent
Incorrect
Un-measurable

## Slide 48: Making it Work: People and Tools
Achieving completeness requires several viewpoints to be taken (demanding a multidisciplinary team approach)
Achieving consistency, conciseness and clarity (removing ambiguity) requires tools that allow the team to communicate, to share information and have a common understanding to avoid having different perceptions but simple enough for the whole team to use
Correctness means we need tools that can verify and validate requirements
There are many similar tools that can accomplish the same goal. We must NOT, however, introduce overly complex tools thinking that they will do a better job. The fundamental maxim of good Systems Engineering is KISS (Keep It Simple - Stupid)

## Slide 49: Process and Tools
Requirements Database
Stakeholder Map
Determine system stakeholders and select key ones for requirements elicitation
Tree Diagram/Analytic Hierarchy Process
Organize and prioritise key stakeholder requirements
The User Requirements defines the expressed requirements of a particular stakeholder or stakeholders
Affinity Diagram
Elicit and capture key stakeholder requirements
Captures how a user expects to interact with a system
Use Case
The Business Requirements provide the rationale and overall business constraints for a system development project
Gather Requirements
Identifies and explores system solutions at different levels to determine System Meta-Solution
Need Mean Analysis
Analyses expressed requirements into their atomic form to identify and clarify missing and ambiguous requirements
Systemic Textual Analysis
Generates and organizes system generic functionality necessary to achieve the Operational Requirement
Viewpoint/Functional Analysis
Captures and shows how the component functionality of a system must cooperate to deliver the Operational Requirement
Function Flow Diagram
Determine the necessary generic System Functionality
Captures the potential functional failure modes, effects and causes to identify remedies ab initio
Functional Failure Mode and Effect Analysis
Identifies causal paths for potential system sensitivities
Flow Sensitivity Analysis
Determine the Emergent Functionality
Cross checks requirements for consistency and completeness
Quality Function Deployment 1
Analyse and Validate Requirements
Specify
Requirements
Determine Validation and Verification methods for each requirement and specify V& V Requirements
Verification Compliance Matrix
The System Requirements defines the measurable design requirements for the system

## Slide 50: Summary
The nature of Stakeholder Expressed Requirements has been discussed. They are often incomplete, inconsistent, rambling, incorrect, ambiguous and un-confirmable
The Holistic Requirements Model is shown to help “untangle” the requirements mess!
  Operational
  Functional
  Non-functional
    Performance
    System
    Implementation
System complexity demands a team approach which in turn demands a structured process and a common tool set
Understanding requirements requires us to take several perspectives and to review and check our understanding
Notes: 32