## Slide 1: Determine System Requirements
Requirements Database
Stakeholder Map
Determine system stakeholders and select key ones for requirements elicitation
Tree Diagram/Analytic Hierarchy Process
Organize and prioritise key stakeholder requirements
The User Requirements defines the expressed requirements of a particular stakeholder or stakeholders
Affinity Diagram
Elicit and capture key stakeholder requirements
Captures how a user expects to interact with a system
Use Case
The Business Requirements provide the rationale and overall business constraints for a system development project
Gather Requirements
Identifies and explores system solutions at different levels to determine System Meta-Solution
Need Mean Analysis
Analyses expressed requirements into their atomic form to identify and clarify missing and ambiguous requirements
Systemic Textual Analysis
Generates and organizes system generic functionality necessary to achieve the Operational Requirement
Viewpoint/Functional Analysis
Captures and shows how the component functionality of a system must cooperate to deliver the Operational Requirement
Function Flow Diagram
Determine the necessary generic System Functionality
Captures the potential functional failure modes, effects and causes to identify remedies ab initio
Functional Failure Mode and Effect Analysis
Identifies causal paths for potential system sensitivities
Flow Sensitivity Analysis
Determine the Emergent Functionality
Cross checks requirements for consistency and completeness
Quality Function Deployment 1
Analyse and Validate Requirements
Specify
Requirements
Determine Validation and Verification methods for each requirement and specify V& V Requirements
Verification Compliance Matrix
The System Requirements defines the measurable design requirements for the system

## Slide 2: Create System Design Concept & Design System
Determine the factors that are most likely to influence the robustness of a nominal design
Design 2 Noise Matrix
Identifies and captures the factors that influence the performance of a system output
Parameter Diagram
Qualitative Robustness and Critical Parameter Analysis
Identify and document the potential failure modes, Effects and Causes
Design Failure Mode and
Effects Analysis
Use models or physical Designed Experiments to characterise the transfer function and thereby robustness of the system design.
Quantitative Robustness Analysis
Designed of Experiments
Simulation and Modelling
Parameter & Tolerance Design
Update QFD 2 with the design parameter target values and as appropriate - tolerances
Quality Function Deployment 2`
Update System Definition and Sub-System Requirements and associated Sub-System Verification Requirements
Requirements Database
Determines the natural structure of a system that can be exploited
N2 Analysis
Determines candidate system architectures with minimal interfaces
Logical System Architecting
Identifies and captures all possible functional solutions to a system design problem and thereby determine suitable candidate system concepts
Function Means Analysis
Compares candidate system concepts against a set of criteria
Pugh Matrix
Verify System Concept Solution meets the System Requirements and allocation of Sub-System Requirements
Quality Function Deployment 2
Use Engineering Modelling, Simulation and Analysis to undertake preliminary design and feasibility
Preliminary Design and Feasibility
Create Candidate System Concepts
Create System Definition and Sub-System Requirements and associated Sub-System Verification Requirements
Requirements Database
Use quantitative models to explore solution space to find robust optimum and thereby determine design parameter settings and tolerances

## Slide 3: Verify and Validate System
Reliability Block Diagram
Model System Failures as a Fault Tree
Fault Tree Analysis
Model the system design to predict the system reliability
Realisation System Modelling and Analysis
Identifies sequence of logical process steps (functions) of the realisation system
Sequence Diagram
Identify and document the potential failure modes, Effects and Causes
Process Failure Mode and
Effects Analysis
Update Verification Compliance Matrix
Verification Compliance Matrix
Assess supportability through predicted
reliability and operational analysis
Supportability Assessment
Understand the System Operation
Operational Analysis
Check that System Concept Solution is realizable and determine critical realization parameters and target values
Quality Function Deployment 3
For the critical realization parameters determine the Assurance Requirements and target values
Quality Function Deployment 4
Perform Verification Activities and collect verification evidence
Collect Verification Evidence
Design and perform tests
Requirements Database
Identifies and captures the factors that influence the performance of a system output
Parameter Diagram