## Slide 2
Analyse Requirements
Determine the Generic System Functionality Using
Viewpoint or Functional Analysis
This Session
Will introduce and provide an opportunity to practise two tools for determining the generic functionality of a system:
  Functional Analysis
  Viewpoint Analysis

## Slide 3: Getting at the Basic Requirements
Systemic Textual Analysis can help us analyse the expressed requirements and begin the discovery of the “unspoken” requirements. There is no guarantee, however, that it will find them all – we have to adopt another approach – experience and common sense
Systemic
Textual
Analysis
We can “get at” the unspoken requirements by identifying the system functionality

## Slide 4: Process and Tools
Requirements Database
Stakeholder Map
Determine system stakeholders and select key ones for requirements elicitation
Tree Diagram/Analytic Hierarchy Process
Organize and prioritise key stakeholder requirements
The User Requirements defines the expressed requirements of a particular stakeholder or stakeholders
Affinity Diagram
Elicit and capture key stakeholder requirements
Captures how a user expects to interact with a system
Use Case
The Business Requirements provide the rationale and overall business constraints for a system development project
Gather Requirements
Identifies and explores system solutions at different levels to determine System Meta-Solution
Need Mean Analysis
Analyses expressed requirements into their atomic form to identify and clarify missing and ambiguous requirements
Systemic Textual Analysis
Generates and organizes system generic functionality necessary to achieve the Operational Requirement
Viewpoint/Functional Analysis
Captures and shows how the component functionality of a system must cooperate to deliver the Operational Requirement
Function Flow Diagram
Determine the necessary generic System Functionality
Captures the potential functional failure modes, effects and causes to identify remedies ab initio
Functional Failure Mode and Effect Analysis
Identifies causal paths for potential system sensitivities
Flow Sensitivity Analysis
Determine the Emergent Functionality
Cross checks requirements for consistency and completeness
Quality Function Deployment 1
Analyse and Validate Requirements
Specify
Requirements
Determine Validation and Verification methods for each requirement and specify V& V Requirements
Verification Compliance Matrix
The System Requirements defines the measurable design requirements for the system

## Slide 5: Where are we?: Analyse Requirements
Assess System Meta-Solution
Determine System Functionality
Determine Emergent Functionality
Verify and Validate Requirements
The iteration may not be simple
Determine “working” Operational Requirement
Determine Non-Functional Performance Requirements
Applying Systems Thinking to the task of analysing requirements tells us that we will need to take various perspectives to help uncover the unspoken requirements

## Slide 6: Top-down & Bottom-up
TOP-DOWN
BOTTOM-UP
Super-System
System
Component
Subsystem
Viewpoint Analysis
Functional Analysis

## Slide 7: Functional Analysis
What is it?
Functional Analysis is a tool that can help a multi-disciplinary team identify and structure the Generic System Functionality of a System based on a previous solution
When to use it?
When attempting to determine the functionality of a component or simple subsystem
How does it work?
The approach adopted is one of using existing design solutions and determining the function of each component or component feature
Functional Analysis is based on the assumption that every component and feature has a purpose
The example above shows an EJ200 temperature sensor that required re-design. Functional Analysis was used to identify the functionality of the existing design to determine the generic functionality

## Slide 8: How to do it?
The approach adopted is one of using existing design solutions and determining the function of each component AND component feature
Step 1: Identify the constituent components AND features
    Step 2: For each component/feature discuss and agree its function – what it does
Step 3: Repeat Step for a alternative design solution to uncover generic functionality
Step 4: If complex create a Function Tree Diagram
In performing a Functional Analysis the process is basically linear

## Slide 9: Step 1: Identify Constituent Components AND Features
Disk
Void
Priming
Composition/Lighting
Features on Face
Washer
Transfer Mix
Lip Varnish
Liner
Composition
Cup
Example: AA Tracer

## Slide 10: Step 2: Discuss and Agree Functionality
Disk
Prevents Moisture Ingress From Propellant
Control Tracer Lighting Pressure
Void
Provide Space for Disk Collapse
Priming Composition/Lighting
Lights Coloured Light Generator (CLG)
Protects CLG from Barrel Pressure
Features on Face
Increase Surface Area
Washer
Control (cokes) Pressure on Face of Tracer
Transfer Mix
Transfer Ignition
Lip Varnish
Seals Disk and Lip
Liner
Protect Against Set-Back
Maintain Cigarette Burn
Composition
Generate Coloured Light
N.B Pellets to aid Mfg.
Provides Oxygen & Fuel
Glues Components
Cup
Retain Tracer Unit

## Slide 11: EJ200 Temperature Sensor

## Slide 12: Step 3: Repeat for an Alternative Design
Our aim is to identify the Generic System Functionality – existing system designs, potentially will have every type of functionality:
  Generic
  Solution dependent
  Legislation dependent
  Architectural
  Emergent
By repeating the exercise with a similar item – i.e. a design solution that achieves the same Operational Requirements the generic functionality can be identified through repetition
Alternatively common sense can be used

## Slide 13: Step 4: If Complex, Convert to a Tree Diagram
Once the functionality has been determined it is useful to convert the list into a Tree Diagram

## Slide 14: Exercise – Functional Analysis
In small groups
  Examine the simple object provided by the tutor to identify each component and feature
  For each component or feature determine its functionality
  Be prepared to share your outcome with the rest of the class
Time 20 minutes

## Slide 15: Functional Analysis
Pros
  Simple tool for identifying component/subsystem functionality
  It can help to gain more understanding about the component/subsystem
  Provides a documented reusable analysis
  When used within a team context it allows the whole team to share information and agree a common understanding
Cons
  Particular items may lead to unnecessary functionality – non-generic functionality – leading to repetition of previous designs (and their drawbacks)
  Only works successfully at the component/subsystem level. Higher level systems are amenable to Functional Analysis but often generate functions at all levels resulting, potentially, in over-emphasis of unimportant functions and under-emphasis of important functions
Notes: 23

## Slide 16: Top-down & Bottom-up
TOP-DOWN
BOTTOM-UP
Super-System
System
Component
Subsystem
Viewpoint Analysis
Functional Analysis

## Slide 17: Viewpoint Analysis
What is it?
  Viewpoint Analysis is a tool that can help a multidisciplinary team identify and structure the requirements of a system
Why do it?
  To identify the required functionality necessary for a system to achieve its Operational Requirement
When to use it?
  Whenever attempting to determine and analyse a set of requirements.
  Particularly useful when there is a small number of customer requirements
How does it work?
  The approach adopted is one of divergent and convergent thinking to generate and structure the requirements.
  The system is examined from two viewpoints
    Functional Viewpoint
    Non-functional Viewpoint
  The approach identifies the natural structure between the functional requirements and how the non-functional requirements impact on them
The example above is the output of a Viewpoint Analysis. It is a Tree Diagram of the system functionality necessary to achieve the Operational Requirement . The “bubbles” contain constraints on that functional structure at the point they impact

## Slide 19: The Viewpoints
The Non-functional Viewpoint
  Requirements that are constraints
The Functional Viewpoint:
  Requirements that are functions deemed necessary for the system to achieve its Operational Requirement
  There are two types of functional viewpoint
    EXTERNAL or BOUNDING: An external or bounding viewpoint is a view of the system from the outside – this highlights external functionality of the system of interest particularly life-cycle functions
    INTERNAL or DEFINING: An internal or defining viewpoint is a view of the system from the inside and is used to describe the internal function of the system of interest
Notes: 7

## Slide 20: How to do it: Viewpoint Analysis Process
Step 1
Requirements Generation
Step 2
Viewpoint Separation
Step 3
Functional Viewpoint Structuring
Step 4
Functional Viewpoint Grouping
Step 5
Functional Viewpoint Structure Chart
Step 6
System Viewpoint Structure Chart
Notes: 9

## Slide 21: Step 1: Requirements Generation
The first stage is to generate the requirements for the system that will make up the functional and non-functional viewpoints
It is important to remember that any customer requirements will not be complete and the team WILL have to “add” obvious (basic) requirements
The approach is for the team to “brainstorm” and write down all possible requirements using sticky notes. There is NO sorting at this point
A key point to note here is that the requirements will come from the
  customer requirements document,
  legislative documents
  experience of the team
The intention is to “brainstorm” requirements not solutions (any solutions should be turned into requirements)
Notes: 10

## Slide 22: We are after Functions
The focus when performing a Viewpoint Analysis is to encourage the team to brainstorm the FUNCTIONS necessary to deliver the Operational Requirement
Like all brainstorming sessions, criticism must be avoided and therefore the activity will also generate Non-functional requirements (including solutions) – this is not a bad thing. Such Non-functional requirements can infer functions
We do need, however, an Operational Requirement for the System of Interest.
  If none exists the starting point for a Viewpoint Analysis is to develop a “Working Operational Requirement”
  If one does exist we need to check that it truly reflects the purpose of the system at the right level

## Slide 23: Example: Intelligent Washing Machine
Product Brief
This machine will replace our existing top of the range model. It will be of standard size and take a standard load.
The machine must be easy to use and will be capable of determining the load make up and fabric type and of determining the ‘best’ cleaning cycle. It will detect mixed loads and where necessary inform the user of extreme loads.
The cost must be within 15% of the existing machine price. The machine must conform to EU safety standards.
The style must be distinctive and attractive. The machine will use domestic water and currently available detergents. Standard electricity supplies will provide the power source.
It will operate at appropriate temperatures and wash cycles most suitable for the fabric type, which are determined by the machine.
The user will have the facility to check the wash cycle and override the machine decision. The machine will rinse and spin-dry the clothing as appropriate to load and type.
Note: There is an assumed Meta-solution of a water-based electrically powered system

## Slide 24: Step 1: A “Working Operational Requirement”
In the example “customer” requirements document there is no clear obvious Operational Requirement – we need to develop one
A good approach here is to get all teams members to draft their own – remember the 18 word target (but do not get hung-up on it – 25 words is okay, as might be 13!)
In this case:
To intelligently wash domestic fabric items effectively and efficiently with the minimum of human intervention
It may be necessary to define what is meant by:
Intelligently
Effectively
Efficiently
This is the “Working OR” – a starting point! It actually is not a particularly “good” requirements because in its present form not measurable! – BUT trying to be “perfect” at this point can be nugatory work

## Slide 25: The Big Question!
What will the system have to do in order to intelligently wash domestic fabric items effectively and efficiently with the minimum of human intervention?

## Slide 26
“to deliver hot water and controllable space heating in a multi-room dwelling with optimum energy usage”

## Slide 27: Step 1 Output: The Viewpoint Requirements Diagram
Door
Maintain
W/M
Accessibility
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Safety
Easy to
Use
Top of
range
Drum
User
instructions
Water
Standard Size
5Kg
Load
Interlocks
Testing
Heat
Water
Controls
User input
Rinse
Spin
Energy
Efficient
Control
Temp
Detect Load
Make-up
Design IWM
Transport
Drain
Water
Reliable
Vibration
Disposal
Cost
Cycle
Display
Conditioner
type
Detergent
Types
Style
Automatic
Cycle
Selection
Filter
water
Wash Time
Delicates
Noise
.90dB
Unload
Install
Standard
Fittings
Measure dirt
Wash
Fill with
water
Power
connection
Distribute
Power
Measure H2O
hardness
Weight
Adjustable
Feet
Power
Supply
Status
Display
Override
Intelligent
Spin Speed
>1600rpm
Colour
Supply
M/C
Mfg.

## Slide 28: The team use their experience and common sense to introduce basic, assumed and delighter requirements
Door
Maintain
W/M
Accessibility
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Easy to
Use
Top of
range
Drum
User
instructions
Water
Standard Size
5Kg
Load
Interlocks
Testing
Heat
Water
Controls
User input
Rinse
Spin
Energy
Efficient
Control
Temp
Detect Load
Make-up
Design
Transport
Drain
Water
Reliable
Vibration
Disposal
Cost
Cycle
Display
Conditioner
type
Detergent
Types
Style
Automatic
Cycle
Selection
Filter
water
Wash Time
Delicates
Noise
.90dB
Unload
Install
Standard
Fittings
Wash
Fill with
water
Power
connection
Distribute
Power
Measure H2O
hardness
Weight
Adjustable
Feet
Power
Supply
Status
Display
Override
Intelligent
Spin Speed
>1600rpm
Colour
Supply
M/C
Mfg.
Maintain
W/M
Accessibility
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Safety
Testing
Controls
Control
Temp
Design IWM
Transport
Drain
Water
Disposal
Cycle
Selection
Filter
water
Wash Time
Delicates
Unload
Install
Standard
Fittings
Measure dirt
Fill with
water
Power
connection
Distribute
Power
Measure H2O
hardness
Weight
Supply
M/C
Mfg.
Not expressed

## Slide 29: Functions not Solutions
Step 1 of VPA demands that the team “brainstorm requirements and not solutions”
In practice this is impossible and actually not desirable, people will naturally tend to think in terms of solutions – which is the “how” rather than the “what”. Hence there is the need to convert the solutions into requirements – into logical functions.
Examples
      Object Function
      Front door Load clothes
      Spinning drum Extract water
This conversion can be done as the brainstorm progresses or after the brainstorm has finished

## Slide 30: Functions not Solutions
Maintain
W/M
Accessibility
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Safety
Easy to
Use
Top of
range
User
instructions
Water
Standard Size
5Kg
Load
Testing
Heat
Water
Controls
User input
Rinse
Energy
Efficient
Control
Temp
Detect Load
Make-up
Design IWM
Transport
Drain
Water
Reliable
Vibration
Disposal
Cost
Cycle
Display
Conditioner
type
Detergent
Types
Style
Automatic
Cycle
Selection
Filter
water
Wash Time
Delicates
Noise
.90dB
Unload
Install
Standard
Fittings
Measure dirt
Wash
Fill with
water
Power
connection
Distribute
Power
Measure H2O
hardness
Weight
Power
Supply
Status
Display
Override
Intelligent
Spin Speed
>1600rpm
Colour
Supply
M/C
Mfg.
Door
Drum
Interlocks
Spin
Adjustable
Feet

## Slide 31: Comments
Door
Load
Dirty Items
Drum
Interlocks
Prevent
Early Access
Control Access
Spin
Extract Excess
Water
Adjustable
Feet
Level M/C
“Door” is a solution and has been transferred into its logical function. What the door does.
“Adjustable feet” is a solution and has been transferred into its logical function.
“Spinning” could be viewed as a function (it passes the “ing” test) but it is, in this context, a solution.
“Interlocks” is a solution to “prevent early access”. This is actually OK, but negative. It is better to try and write the function as a positive action
The “Drum” is a solution but one that has multiple functionality – e.g. wash, spin, rinse etc. Need to check that all the functionality has been identified

## Slide 32: Functions as Verb Noun Phrases
When brainstorming requirements we are often economical with our language and describe functions by just the verb
This is not a bad thing to do, the requirements generation step is about quantity not quality
It is, however, good practice to review the brainstormed requirements and convert verb only functions into full verb noun descriptions
For example
Testing
Rinse
Test M/C
Rinse Load

## Slide 33: Defining “good” Functions
A System Function defines something the System has to do – it’s a job, a task, an activity
Functions are defined as a
The NOUN defines the object the verb acts on. It should be a concrete noun
  something that can be touched, seen, tasted, smelt or heard.
Beware of abstract nouns
  these are things you cannot touch, see, hear, smell or taste (but can sometimes measure) like reliability, safety, style, etc.
The VERB is also important to define correctly
Look for VERBS that don’t imply a solution – BUT later when designing the system will allow you to explore all the solution options
  Deliver Toast (good)
  Eject Toast (bad because it suggests a “pop-up” mechanism)
Do explore different verbs – we always have choice.
Try to use imperative verbs – command verbs - wherever possible
VERB NOUN

## Slide 34: Functions as Verb Noun Phrases
Maintain
W/M
Accessibility
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Safety
Easy to
Use
Top of
range
User
instructions
Water
Standard Size
5Kg
Load
Testing
Heat
Water
Controls
User input
Rinse
Energy
Efficient
Control
Temp
Detect Load
Make-up
Design
Transport
Drain
Water
Reliable
Vibration
Disposal
Cost
Cycle
Display
Conditioner
type
Detergent
Types
Style
Automatic
Cycle
Selection
Filter
water
Wash Time
Delicates
Noise
.90dB
Unload
Install
Standard
Fittings
Measure dirt
Wash
Fill with
water
Power
connection
Distribute
Power
Measure H2O
hardness
Weight
Power
Supply
Status
Display
Override
Intelligent
Spin Speed
>1600rpm
Colour
Supply
M/C
Mfg.
Load
Dirty Items
Control Access
Extract Excess
Water
Level M/C

## Slide 35: Functions as Verb Noun Phrases
Maintain
W/M
Accessibility
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Safety
Easy to
Use
Top of
range
User
instructions
Standard Size
5Kg
Load
Test M/C
Heat
Water
Controls
User input
Rinse Load
Energy
Efficient
Control
Temp
Detect Load
Make-up
Design M/C
Transport
M/C
Drain
Water
Reliable
Vibration
Dispose M/C
Cost
Cycle
Display
Conditioner
type
Detergent
Types
Style
Automatic
Cycle
Selection
Filter
water
Wash Time
Delicates
Noise
.90dB
Unload
Clean Items
Install M/C
Standard
Fittings
Measure dirt
Wash
Load
Fill with
water
Power
connection
Distribute
Power
Measure H2O
hardness
Weight
Power
Supply
Status
Display
Override M/C
Intelligent
Spin Speed
>1600rpm
Colour
Supply
M/C
Mfg. M/C
Load
Dirty Items
Control Access
Extract Excess
Water
Level M/C
Water

## Slide 36: Do Take a Lifecycle View
When brainstorming system functions we should also consider the life cycle functions like:
  Design IWM
  Manufacture IWM
  Test IWM
  Sell IWM
  Operate IWM
  Support IWM
  Etc.
These functions are likely to be part of the External Functional Viewpoint but are important to include because:
  They are “systems” in their own right that may have to be developed
  They are sources of further constraints that will affect the design
  We haven’t yet defined the system boundary (Step 3)

## Slide 37: Step 2: Viewpoint Separation
The second step in Viewpoint Analysis is to separate the functional and non-functional requirements to provide the two basic viewpoints
Care should be exercised when identifying the functions that form the functional viewpoint
  Function descriptions are a verb or a verb noun phrase where the verb is typically an imperative verb and the noun is a common noun
  Functions transform inputs to outputs
  Beware of pseudo functions
Remember customers tend to specify solutions (NFI) and performance (NFP and NFS), we should consider every requirement to see if it implies a function - which we should deduce and record on a new sticky note
Our aim here is identify all possible functionality of the proposed system – we can always choose not to implement functionality, but if it is not identified in the first place we will never have the opportunity to make that decision.
Notes: 12

## Slide 38: Typical Step 2 Output
Maintain
W/M
Accessibility
Load
Dirty Items
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Safety
Easy to
Use
Top of
range
User
instructions
Water
Standard Size
5Kg
Load
Control Access
Test M/C
Heat
Water
Controls
User input
Rinse Load
Extract Excess
Water
Energy
Efficient
Control
Temp
Detect Load
Make-up
Design M/C
Transport M/C
Drain
Water
Reliable
Vibration
Dispose M/C
Cost
Cycle
Display
Conditioner
type
Detergent
Types
Style
Automatic
Cycle
Selection
Filter
water
Wash Time
Delicates
Noise
.90dB
Unload Clean Items
Install M/C
Standard
Fittings
Measure dirt
Wash Load
Fill with
water
Power
connection
Distribute
Power
Measure H2O
hardness
Weight
Power
Supply
Level M/C
Status
Display
Override M/C
Intelligent
Spin Speed
>1600rpm
Colour
Supply
M/C
Functional
Non-functional
Not Clear
Mfg. M/C

## Slide 39: It’s best to be pedantic
Controls
User input
Cycle
Display
Cycle
Selection
Power
connection
Power
Supply
Status
Display
Not Clear
Supply
Power
230V 50Hz AC
Control
Wash Cycle
Interface to
Power
BS 13653 Plug
& socket
Display
Cycle
Display
Status
Select
Cycle
Receive user
instructions
Convert solutions
into functions
Capture Non
Functional
Requirements
Convert solutions
into functions
Capture Non
-functional
Requirements

## Slide 40: Typical Step 2 Output
Maintain
M/C
Accessibility
Load
Dirty Items
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Safety
Easy to
Use
Top of
range
User
instructions
Water
Standard Size
5Kg
Load
Control Access
Test M/C
Heat
Water
Rinse Load
Extract Excess
Water
Energy
Efficient
Control
Temp
Detect Load
Make-up
Design M/C
Transport M/C
Drain
Water
Reliable
Vibration
Dispose M/C
Cost
Conditioner
type
Detergent
Types
Style
Automatic
Filter
water
Wash Time
Delicates
Noise
<90dB
Unload
Clean Items
Install M/C
Standard
Fittings
Measure dirt
Wash Load
Fill with
water
Distribute
Power
Measure H2O
hardness
Weight
Level M/C
Override M/C
Intelligent
Spin Speed
>1600rpm
Colour
Supply
M/C
Functional
Non-functional
Supply
Power
Control
Wash Cycle
Interface to
Power
Display
Cycle
Display
Status
Select
Cycle
Receive user
instructions
230V 50Hz AC
BS 13653 Plug
& socket
Mfg. M/C

## Slide 41: Step 3: Functional Viewpoint Structuring
The Non-functional Viewpoint requirements are temporarily discarded and consideration is given to logically structuring the Functional Viewpoint requirements
The first step in structuring the Functional Viewpoint requirements is to identify the External and Internal Functional Viewpoint requirements
This effectively defines the “prime system” and those systems elements in its environment that it will have to interact with (which we may have to consider in more detail in order to design a “better” prime system)
Notes: 14

## Slide 42: Typical Step 3 Output
Maintain
M/C
Load
Dirty Items
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Control Access
Test M/C
Heat
Water
Rinse Load
Extract Excess
Water
Control
Temp
Detect Load
Make-up
Design M/C
Transport M/C
Drain
Water
Dispose M/C
Filter
water
Unload
Clean Items
Install M/C
Measure dirt
Wash Load
Fill with
water
Distribute
Power
Measure H2O
hardness
Level M/C
Override M/C
Supply
M/C
Internal Viewpoint
Supply
Power
Control
Wash Cycle
Interface to
Power
Display
Cycle
Display
Status
Select
Cycle
Receive user
instructions
External Viewpoint
Some functions could be inside or outside the prime system. Where we decide to put them defines the system boundary. We need to think carefully about these. Will they lead to design solutions that will be part of the prime system
Mfg. M/C

## Slide 43: Final Step 3 Output
Maintain
M/C
Load
Dirty Items
Load
Detergent
Load
Conditioner
Load
Water Softener
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Control Access
Test M/C
Heat
Water
Rinse Load
Extract Excess
Water
Control
Temp
Detect Load
Make-up
Design M/C
Transport M/C
Drain
Water
Dispose M/C
Filter
water
Unload
Clean Items
Install M/C
Measure dirt
Wash Load
Fill with
water
Distribute
Power
Measure H2O
hardness
Level M/C
Override M/C
Supply
M/C
Internal Viewpoint
Supply
Power
Control
Wash Cycle
Manage
Power
Display
Cycle
Display
Status
Select
Cycle
Receive user
instructions
External Viewpoint
Receive
Water Supply
Remove
Waste
Supply
Water
Receive
Waste
Mfg. M/C
By separating and categorising requirements we start to simplify our understanding which often leads to identifying additional necessary functionality (requirements)

## Slide 44: Step 4: Functional Viewpoint Grouping
The next step is to logically group the functions together so that at any one level of grouping there is a maximum of 5 functions ( 7 – 2 allowing “headroom” for undiscovered functions)
The groups should be logical and named
  If you have difficulty deciding a name the grouping is not logical – look for another grouping
  Choose a name that is a Verb Noun combination to maintain the emphasis on functions (we tend to drift back to object-oriented thinking)
Notes: 16

## Slide 45
Maintain
M/C
Test M/C
Design M/C
Disposal M/C
Distribute
Power
Level M/C
Supply
Power
Manage
Power
Receive
Water Supply
Remove
Waste
Interface
to services
Override M/C
Display
Cycle
Display
Status
Receive user
instructions
Interface to User
Control
Wash Cycle
Select
Cycle
Manage Cycle
Rinse Load
Wash Load
Clean Items
Detect
Load Colour
Detect
Load Weight
Detect Fabric
Type
Measure dirt
Measure H2O
hardness
Detect Load
Make-up
Sense Wash Conditions
Drain
Water
Extract Excess
Water
Filter
water
Fill with
water
Heat
Water
Control
Temp
Manage
Temperature
Manage Water
Load
Dirty Items
Load
Detergent
Load
Conditioner
Load
Water Softener
Control Access
Unload
Clean Items
Load Cleaning
Agents
Load Machine
Supply
Water
Receive
Waste
Transport M/C
Install M/C
Supply
M/C
Provide
machine
Provide Services
Mfg. M/C
Manage Wash
Realise M/C
Support M/C
External Viewpoint
Internal Viewpoint
Operate IWM

## Slide 46: Step 5: Functional Viewpoint Structure Chart
The penultimate stage is to convert the structured viewpoint affinity diagram into a Functional Viewpoint Structure Chart
We put the external viewpoint functions at the same level as the prime system – it is usual to capture the prime system as the function “Operate XYZ System”
  The purpose here is to elevate these critical lifecycle and interface functions such that their importance is recognised early because:
    We need to design for
      Manufacture
      Sales
      Disposal
      Maintenance
      Etc.
    “design for” means “design in”
As we construct the Functional Viewpoint Structure Chart, we should review it to identify any further functionality
Notes: 18

## Slide 47: Typical Step 5 Output
Design M/C
Support
M/C
Realise M/C
Supply
Water
Supply
Power
Remove
Waste
Provide Services
Supply
MC
Transport
M/C
Install M/C
Provide
Machine
Operate
IWM
Washing
System
Sense Wash
Conditions
Interface
to Services
Level M/C
Distribute
Power
Load
Machine
Manage
Wash
Detect Load
Make up
Detect Load
Colour
Detect Load
Weight
Detect Fabric
Type
Measure
Dirt
Measure H20
Hardness
Receive
Water
Manage
Power
Remove
Waste
Load Dirty
Items
Unload
Clean Items
Control
Access
Load Clean
Agents
Load
Detergents
Load
Conditioner
Load Water
Softener
Manage
Water
Clean Items
Manage
Cycle
Control
Wash Cycle
Select
Cycle
Wash
Load
Rinse
Load
Extract XS
Water
Drain Water
Fill Water
Filter Water
Manage
Temperature
Heat Water
Control H2 O Temp
Interface to User
Override
M/C
Display
Status
Display
Cycle
Rx User
Instructions
Test M/C
Mfg. M/C
Dispose
M/C
Maintain
M/C
Functions that appear “not to fit” should be investigated!

## Slide 48: Typical Step 5 Output
Design M/C
Support
M/C
Realise M/C
Supply
Water
Supply
Power
Remove
Waste
Provide Services
Supply
MC
Transport
M/C
Install M/C
Provide
Machine
Operate
IWM
Washing
System
Sense Wash
Conditions
Interface
to Services
Distribute
Power
Load
Machine
Manage
Wash
Detect Load
Make up
Detect Load
Colour
Detect Load
Weight
Detect Fabric
Type
Measure
Dirt
Measure H20
Hardness
Receive
Water
Manage
Power
Remove
Waste
Load Dirty
Items
Unload
Clean Items
Control
Access
Load Clean
Agents
Load
Detergents
Load
Conditioner
Load Water
Softener
Manage
Water
Clean Items
Manage
Cycle
Control
Wash Cycle
Select
Cycle
Wash
Load
Rinse
Load
Extract XS
Water
Drain Water
Fill Water
Filter Water
Manage
Temperature
Heat Water
Control H2 O Temp
Interface to User
Override
M/C
Display
Status
Display
Cycle
Rx User
Instructions
Test M/C
Mfg. M/C
Dispose
M/C
Maintain
M/C
Have we got everything? Are we missing logical generic functionality?

## Slide 49: Step 6: Non-functional Viewpoint Structure
The final stage in Viewpoint Analysis is to re-introduce the Non-functional Requirements but at their most appropriate point in the Functional Viewpoint Structure Chart
This can be achieved by considering each of the Non-functional Viewpoint Requirements and finding the “best” place for it to sit in the functional viewpoint structure
This step can be very useful in identifying further missing requirements – particularly Non-functional Performance Requirements. All system functions identified must have associated Non-Functional Performance Requirements
Notes: 20

## Slide 50
Design M/C
Support
M/C
Realise M/C
Supply
Water
Supply
Power
Remove
Waste
Provide Services
Supply
MC
Transport
M/C
Install M/C
Provide
Machine
Operate
IWM
Washing
System
Sense Wash
Conditions
Interface
to Services
Level M/C
Distribute
Power
Load
Machine
Manage
Wash
Detect Load
Make up
Detect Load
Colour
Detect Load
Weight
Detect Fabric
Type
Measure
Dirt
Measure H20
Hardness
Receive
Water
Manage
Power
Remove
Waste
Load Dirty
Items
Unload
Clean Items
Control
Access
Load Clean
Agents
Load
Detergents
Load
Conditioner
Load Water
Softener
Manage
Water
Clean Items
Manage
Cycle
Control
Wash Cycle
Select
Cycle
Wash
Load
Rinse
Load
Extract XS
Water
Drain Water
Fill Water
Filter Water
Manage
Temperature
Heat Water
Control H2 O Temp
Interface to User
Override
M/C
Display
Status
Display
Cycle
Rx User
Instructions
Test M/C
Mfg. M/C
Dispose
M/C
Maintain
M/C
Safety
Easy to
Use
Water
Reliable
Cost
Style
Standard
Fittings
230V 50Hz AC
BS 13653 Plug
& socket
User
instructions
Standard Size
Energy
Efficient
Noise
.90dB
Weight
Intelligent
Colour
Automatic
Vibration
Wash Time
Delicates
Conditioner
type
Detergent
Types
Spin Speed
>1600rpm
Sense Water Temp

## Slide 51: Holistic Requirements Model and VPA
Non-
functional
System
Non-
functional
Performance
Functions with no attached sticky notes tell us there are missing NFP requirements

## Slide 52: Other Systems
The Viewpoint Analysis will identify other “systems” that need consideration. These are often the “Life Cycle” functions like Supply, Maintenance, Disposal etc. These could be subject to their own Viewpoint Analysis and will have their own Requirements

## Slide 53: Functional Structure Chart for the Support System
INTELLIGENT WASHING SYSTEM
OPERATE SUPPORT
SYSTEM
MANAGE SS
FACILITIES
SELL IWM SS
OPERATE IWM
MANAGE
PROGNOSIS
MANAGE
CUSTOMER
PERFORM FIX
MANAGE
FAULT
BUILD
IWM SS
DISPOSE
SUPPORT SYS
SUPPORT
SUPPORT SYS
MANAGE
STAFF
TRAIN STAFF
RECRUIT STAFF
MONITOR STAFF
TRANSPORT TECHNIAN
FIX IWM
PROVIDE TECH DATA
PROVIDE TECH ASSIST
REPORT ACTION
DIAGNOSE FAULT
PROVISON SPARES
SELECT VISIT TIME
SCHEDULE TECHNICIAN
RECEIVE CUSTOMER ISSUE
LOG ISSUE
TRACK ISSUES
INFORM PROGRESS
MANAGE WARRANTY
UPDATE IWM HISTORY
INVOICE CUSTOMER
COLLECT IWM HEALTH DATA
UPDATE
IWM
INTERROGATE
IWM
PROGNOSE FAULT
INFORM CUSTOMER
(INCIPIENT FAILURE)
MANAGE FAILURE DATA
COLLECT FAILURE DATA
ANALYSE FAILURE DATA
REPORT FAILURE INFO
MANAGE ISSUE
MANAGE
COMPLAINTS
MANAGE FINANCE

## Slide 54: Exercise: Viewpoint Analysis
In teams:
  Undertake a Viewpoint Analysis for the case study example
  Be prepared to share your viewpoint structure chart with the rest of the group
Time: 60 Minutes

## Slide 55
Manage Water
Interact with User
Manage Space Heating
Predict Room X Temp Profile
Manage Heat
Assess Weather
Receive Power Tariffs
Learn Room X
Properties
Program IHS (set up)
Receive Weather Forecast
Calculate Solar Heating
Deliver Heat Addition
Calculate Heat Addition
Heat Water
Modify Room X Temp Profile
Calculate Room X Temp Profile
Set Room X Temp
Calculate Thermal Losses
Inform User
Sense Room Temp
Measure
Water
Temp
Control Water
Temp
Store Hot Water
Measure Local Weather
Manage Performance
Monitor IHS
Report Performance
Determine Fault Code
Dispose IHS
Mfg IHS
Sell IHS
Design IHS
Deliver IHS
Install IHS
Survey Building
Support IHS
Repair IHS
Maintain IHS
Operate IHS
The Intelligent heating Systems

## Slide 56: Concerns
Teams are often concerned with “is the diagram right?”
The purpose of viewpoint analysis is to generate more knowledge about a proposed system. As long as the viewpoint structure represents the whole of the problem, it does not matter if it is different to another potential viewpoint structure
Manage
Wash
Manage
Water
Clean Items
Manage
Cycle
Control
Wash Cycle
Select
Cycle
Agitate
Items
Rinse
Items
Extract XS
Water
Drain Water
Fill With
Water
Filter Water
Manage
Temp
Heat Water
Control Temp
Manage
Wash
Perform
Wash
Control
Wash
Control
Wash Cycle
Control
Temp
Filter Water
Fill
Water
Extract XS
Water
Drain Water
Rinse Items
Agitate
Items
Heat Water
Common Purpose
(Group on the noun)
Common Themes
(Group on the verb)
Select
Cycle

## Slide 57: Tying up loose ends
Viewpoint Analysis is very good at identifying 80% - 90% of the system functionality – we need to do something else to find the other 10% - 20%
If a Systemic Textual Analysis has been undertaken it should be updated with the new derived requirements from the Viewpoint Analysis
If a Systemic Textual Analysis has not been undertaken – start one now.

## Slide 58: Summary : Viewpoint Analysis
Pros
  Simple tool for diagrammatically showing the hierarchy/structure of functional and non-functional requirements
  It can highlight requirements missing from the original source (customer/stakeholder) requirements - and identify and emphasise life cycle aspects: it helps us be holistic
  It can help to structure the concept design and project management
  It can help to gain more understanding about the system and what all the stakeholders expect
  It can help in showing the various stakeholders that you understand what they are after
  When used within a team context it allows the whole team to share information and agree a common understanding
Cons
  Grouping can be difficult since many functions could reside in several groups
  Does not show cross links between functions
Notes: 23

## Slide 59: Summary
Viewpoint/
Functional Analysis
Systemic Textual
Analysis
Viewpoint and/or Functional Analysis helps identify and record in a structured diagrammatic fashion the generic functionality of a system uncovering unspoken requirements and implying further ones