## Slide 1: Design System A Systems Approach to Robust Design
Secondary Information Goes Here
This Session:
Explains the Systems Approach to Optimising and Refining [the] Solution Concept
Emphasise the importance of finding the“Robust Optimum”

## Slide 2: Where are we: Optimise Solution Concept
Purpose :
  To explore and characterise the design space of the selected system concept design(s) in order to identify the robust optimum
Outcomes :
  The robust optimum concept design
  Requirements flowed down to subsystem level
Design Space?
Robust Optimum?

## Slide 3: System Design Optimization
The performance of a system will be influenced by a number of system design parameters – those variables that the designer selects target values for to achieve the desired level of system performance
The challenge for the system designer is to find the best target or nominal values for the system design parameters in order to meet or, better still, exceed the performance requirements
For example if a drum is selected as the means to the “wash items” function of a washing machine
The quality of the wash will depend on:
  Speed of rotation
  Drum diameter
  Drum depth
  Drum material
  etc.
Steel 708430
diameter
depth
Notes: 4
4

## Slide 4: Where is the best place to be?
System
Performance
Design
Parameter X2
Design
Parameter X1
Required
Customer
Performance
What would be the best target or nominal values for X1 and X2 to give best possible performance?
How System Performance Varies as X1 and X2 vary is the Design Space

## Slide 5: The Best Place – the Global Optimum?
System
Performance
Design
Parameter X1
Required
Customer
Performance
Target Value of X1
Target Value of X2
Having found the global optimum we can “work backwards” to specify the target values for the design parameters
Design
Parameter X2

## Slide 6: All Systems are Subject to Noise
Required
Customer
Performance
Variation in X1 due to noise
Variation in X2 due to noise
Variation in Performance
This design is sensitive to variation and its performance will frequently fall short of the customer’s expectation
What can be done to reduce the variation in performance?
In practice, the design target value will not be met for many reasons it will be subject to variation – we call this variation NOISE

## Slide 7: Many Sources of Noise Variation
There are three groups:
  External: The environment and the load under which a system must function are the two main external sources of variation
      Temperature, humidity, vibration
      Operator usage
  Unit-to-Unit Variation: The variation in a manufacturing process leads to variation in the system from unit-to-unit
      Differences in diameter from machining
      Raw material variation
      Calibration
      Gauge Repeatability & Reproducibility
  Deterioration: As time passes the system characteristics can change leading to a deterioration in performance

## Slide 8: The Classic Strategy: Tighten Tolerances
Required
Customer
Performance
Variation in Performance
The classic reaction to a sensitive design is to set tighter tolerances. This does work but often comes at a great cost.
Set Tight Tolerances for X1
Set Tight Tolerances for X2

## Slide 9: Achieving Design Robustness
A Robust Optimum
New Nominal Value for X1
New Nominal Value for X2
Variation in Performance
This design is less sensitive to variation and will consistently meet the customers expectation

## Slide 10: Robust System Optimisation
Finding the target or nominal values for the system design parameters that deliver best performance may sound like the “optimum design” but can result in sensitive designs that suffer excessive variation in performance, causing customer dissatisfaction.
The optimum design in systems engineering is the robust optimum.
  The best target values for the system design parameters that meet the customer requirements CONSISTENTLY, robust against the effects of variation.
THE ROBUST OPTIMUM
New Nominal Value for X1
New Nominal Value for X2
Variation in Performance
But how can it be achieved in practice?
Notes: 4
4

## Slide 11: Key Tasks and Systems Tools
Determine Critical Design Parameters and Noise Variables
Define Subsystem Requirements
Typical Systems Tools
Simulation Studies
Prototype Tests
Design of Experiments
  Full Factorial
  Response Surface Methods
  Noise Experiments
Quality Function Deployment 2
Perform Parameter and Tolerance Design
Characterise Concept Design Transfer Functions
Typical Systems Tools
P-Diagram
What-Why Table
DFMEA
Simulation studies
Prototype tests
Design of Experiments
  Full Factorial
  Screening Design
  Response Surface Methods
Robust Design & Flow-
down of Requirements
Characterise Design
Notes: 9
9

## Slide 12: Create System Design Concept & Design System
Determine the factors that are most likely to influence the robustness of a nominal design
Design 2 Noise Matrix
Identifies and captures the factors that influence the performance of a system output
Parameter Diagram
Qualitative Robustness and Critical Parameter Analysis
Identify and document the potential failure modes, Effects and Causes
Design Failure Mode and
Effects Analysis
Use models or physical Designed Experiments to characterise the transfer function and thereby robustness of the system design.
Quantitative Robustness Analysis
Designed of Experiments
Simulation and Modelling
Parameter & Tolerance Design
Update QFD 2 with the design parameter target values and as appropriate - tolerances
Quality Function Deployment 2`
Update System Definition and Sub-System Requirements and associated Sub-System Verification Requirements
Requirements Database
Use quantitative models to explore solution space to find robust optimum and thereby determine design parameter settings and tolerances

## Slide 13: We are Talking about Variation and Loss Functions
LSL
USL
Target
m
y
Deviation
from target
Loss = k(y-m)2
Taguchi’s loss function applies to other system outputs and not just cost!
Loss of Y
Variation of X

## Slide 14: Achieving Design Robustness is Therefore
Design robustness is concerned with:
  Exploring the design space to find regions where the desired system performance (Y) is achieved even in the face of variation in the noise factors
  i.e. finding the plateaus and avoiding the peaks and troughs.
Fundamental approach is to:
  Identify the transfer function that quantifies the relationship between the performance requirement and the signal, control and noise factors
  Find the “best” settings for the control factors (design parameters) that optimise the performance requirement while simultaneously reducing the sensitivity to noise
Where is the best place to be?
New Nominal Value for X1
New Nominal Value for X2
Variation in Performance

## Slide 15: Iterate Design: A Systems Approach
System Design
Establish the fundamental design and engineering concepts
Parameter Design
Determination of target values AND
sensitivity to variation – i.e. the loss functions are determined. If a sensitive design, iterate the design by changing the target values
Tolerance Design
Tolerances established based on
sensitivity analysis. Robust components
do not need a tight tolerance -
sensitive ones do

## Slide 16: Conventional Design
Design Parameter X1
Spec Y
Y = f(X1)
System Output Y
Use the mid point of the customer spec to define the target value for X1
Target for X1
Having determined a target we ask manufacturing for the likely variation around this nominal: Note this may not be the only noise
Oh dear!. The manufacturing noise variation is “transmitted” through the transfer function to give this variation at the output
Transmission of the variation in X1 to Y through the transfer function Y=f(X1)
The requirements for the system output express a range of suitable values

## Slide 17: Traditional Solution
Design Parameter X1
Spec Y
System Output Y
Solution: Tighten the Tolerance! Live with the cost!
Y = f(X1)
Transmission of the variation in X1 to Y through the transfer function Y=f(X1)

## Slide 18: Taguchi’s Parameter Design
Tol X1
X1
Y
Spec Y
Exploit non-linearity to re-specify mean of X1 with same tolerance
ChangeX2
At the new nominal for X1 - Y is insensitive but off target.
Change mean of another design ‘Control’ parameter X2 which has a relationship with Y such that it can bring Y back on target without affecting variance of Y.

## Slide 19: Example: The Intelligent Washing Machine
Start by finding out what the customer wants
Customer satisfaction is affected by:
  Attractive and distinctive
  Cost of purchase
  Running costs
  Washing performance
  Dry performance
  Reliability/Durability
  Ease of use
  Access Ergonomics
  Easy to maintain
  Safety

## Slide 20: Need to Interpret Customer Requirements Technically
QFD 1
Customer Importance
IWM Functions and Features
Wash Sensing
Detect Load Make Up
Measure H20
Hardness
Load Machine
Load Dirty Items
Unload
Load Cleaning Agents
Manage Water
Fill Water
Drain Water
Remove XS Water
Clean Items
Wash
Rinse
Manage
Select Cycle
Control Cycle
Interface to Services
User I/O
Receive user input
Display user
messages
Casing
Customer Requirements
Intelligent Dishwasher
Good Wash
Wash Performance
Dry Performance
Ease of Use
Automation &
Intelligence
Easy to use
Controls
Access
Ergonomics
Cost
Purchase
Running
Long
Reliable
Easy to Maintain
Style
Attractive
How Much
Weighted Importance
Relative Importance
1.0
1.0
5.0
5.0
3.0
1.0
2.0
1.0
1.0
5.0
81.0
23.0
35.0
33.0
57.0
10.0
15.0
25.0
17.0
9.0
76.0
22.0
22.0
72.0
70.0
71.0
Intelligent Washing
Machine
How Much might be:
Drain <2min
FYFR <1%
DTUPC <£8.0
Washing performance is affected by several system functions including the Drain Water Function. Customer research determines that the target for the Drain Water function is less than 2 minutes. The Drain Water Function also has other high level requirements of reliability and cost
Use QFD 1 to translate into Technical Design Requirements

Δ
Δ

## Slide 21: System Design & Requirements Flow Down
Cycle, status in cycle
Determine Load Distribution
Drain Water
Self Monitor
Detect Load make up
Detect H2O hardness
Inform user
Design
Requirements
Element
Requirements
Direction of improvement
Switch
BITE
Weight sensors
Etc .
Activate
pump
Manually activated
7Kg Max .1 res
< 2 mins
FYFR <1%
DTUPC <£8.0
95%
validation
5.6 kg max
EU Limits
Target values
16A 240V Double pole
15 x xyz type
10 l/min +/- 1
FYFR <1%
DTUPC<£8.0
15 type xyz type
3 x XYZ type
Etc.
RFI Tags
Hardness Sensor
The concept design stage (FMA, Pugh, QFD 2) identifies a pump as the solution for the drain water function.
The NFP requirement of:
drain time < 2min
Can be translated in to a subsystem requirements as a target flow rate and allowable variation of 10 +/-1 (litres/min). Below 9 litres/min cannot meet the < 2 min limit. Above 11 litres/min will cause flooding!

## Slide 22: Determining Design Parameter Requirements
A reciprocating pump is selected as the design solution to the “Drain Water” functional requirement.
The pump subsystem requirements flowed down from the system requirements are:
  Flow Rate = 10 litres/min +/-1 litre
  Reliability FYFR < 1%
  DTUPC <£8.00
Where
R = Piston radius (M)
L = Stroke length (M)
B = Back flow (l)
N = Motor speed (rpm)
Tubing
Piston
One way valve
F = (10-6πR2L - B)N
From first principles the transfer function for the flow rate F is

## Slide 23: Target (Nominal) Design
Using:
A Nominal Design exists for
Piston Radius R = 40mm
Stroke Length L = 40mm
Valve Backflow B = 0.002L
Motor Speed N = 50 rpm
It is decided that the valves and motor are to be bought out items with the following specifications (obtained from the OEM catalogues).The piston (and cylinder) and connecting rod will be made in house and using standard tolerances (same as last time)
F = (10-6π402x40 – 0.002)50 = 9.95L/min
F = (10-6πR2L - B)N
 | Make |  | Buy | 
 | Piston Radius R (mm) | Con-rod centre length L (mm) | Valve leakage B (L) | Motor Speed N (rpm)
Target | 40 | 40 | 0.002 | 50
Lower Limit | 39.7 | 39.4 | 0.00185 | 44
Upper Limit | 40.3 | 40.6 | 0.00215 | 56

## Slide 24: Assess Sensitivity of Nominal Design due to Manufacturing Variation
At the extremes of the expected manufacturing variation, the flow rate could vary from 8.5 up to 11.5 l/min – outside the design requirements The current target (nominal) design is not robust against this source of variation.
 | R (mm) | L(mm) | B(L/min) | N(rpm) | F (L/min)
Target | 40 | 40 | 0.002 | 50 | 9.95
High Flow | 40.3 | 40.6 | 0.00185 | 56 | 11.5
Low Flow | 39.7 | 39.4 | 0.00215 | 44 | 8.5
What are we going to do?

## Slide 25: Traditional Strategy: Tighten Tolerances
The design requirement of 10 ± 1L/min can be achieved by tightening the tolerances
It is possible to meet the design requirements by only tightening tolerances of the bought-out elements!
Tolerance Design: tighten the tolerances |  |  |  |  | 
 | R (mm) | L(mm) | B(L/min) | N(rpm) | F (L/min)
High Flow | 40.3 | 40.6 | 0.00194 | 53 | 10.9
Low Flow | 39.7 | 39.4 | 0.00206 | 47 | 9.1
The design requirements can be achieved by tightening the tolerances on the bought-out elements. Looks good BUT costs will increase – usually faster than the losses

## Slide 26: Robust Design Strategy: Parameter Design
A robust design strategy asks for a design iteration to find another point in the solution space that exploits the non-linearity in the system to find a “plateau” where the design is insensitive
 | R (mm) | L(mm) | B(L/min) | N(rpm) | F (L/min)
Target | 20 | 60 | 0.002 | 136 | 9.98
High Flow | 20.3 | 60.6 | 0.00185 | 142 | 10.9
Low Flow | 19.7 | 59.4 | 0.00215 | 130 | 9.1
Parameter Design
Iterate the design to find new target values such as R: 20, L: 60, N: 136 manufacturing variation remains the same

## Slide 27: Searching the “Design Space” for the Robust Optimum
Performance
X2
X1
Robust design requires us to search the design space, not necessarily for the global-optimum, but for the robust-optimum.
Here is the global-optimum! But small variations in X1 and X2 will result in a dramatic fall off in performance. This is a sensitive design
Here is a region of low sensitivity. The performance is “lower” but will be maintained for likely variations in X1 an X2. This is the robust-optimum and would be a robust design
BUT how do we “quickly” find the Robust Optimum?

## Slide 28: Exploring the Design Space
The task is to characterise the design space to “find” the peaks, troughs and plateaus
Approaches include:
  Trial and Error: Searching the design space using judgement, hunches and other magical techniques
Designed Experimentation
  Systematically but scientifically search the design space using Design of Experiments

## Slide 29: Summary
Customers do not like sensitive systems – they appear to be unpredictable
Parameter design provides an approach for finding the robust optimum without resorting to tightening of design tolerances
It does require us however to find an efficient way of searching the design space
At Waters the intention is to have a 5-day Robust Design training programme starting 2017